## Slide 1
Rafsan Jany
Korean Convergence Medical Science
CHROM Phase Lag Analysis
Synthetic Dataset Experiment

## Slide 2
1
Another Dataset
SCAMPS : A Multimodal Dataset For Psychophysiological Studies Of Social Stress [PORTAL]
Total size: -> 2,800 videos (~1.68M frames) -> Each video: 20 seconds long
Ground-truth signals (frame-level & video-level labels): Photoplethysmography (PPG), ECG (inter-beat intervals / RR intervals), Breathing waveform + breathing intervals Heart rate variability (HRV, SDNN), Pulse arrival time (rPAT), Dicrotic wave amplitude Facial action units (10 AUs: brow raise, lip corner puller, jaw drop, eyes closed, etc.) Head pose (rotations)
Waveform sampling: PPG waveforms at 300 Hz Normalized signals
Dataset splits: Video files (RGB frames) Synchronized ground-truth provided as MAT and CSV files

## Slide 3
2
Another Dataset
COHFACE : COntinuous Health and FACE video dataset
Participants: -> 40 healthy subjects. -> Gender: 12 women (30%), 28 men (70%). -> Age: Mean = 35.6 years, Std = 11.47 years.
Recording Sessions: Each subject recorded 4 sessions, about 60 seconds each. Two sessions under studio lighting (controlled) and two under natural lighting (blinds open, no artificial lamps). Total videos: 160.
Video Data: Camera: Logitech HD Webcam C525. Resolution: 640 × 480 pixels. Frame rate: 20 fps. File format: MP4 (AVI container).
Ground-Truth Physiological Signals: Blood Volume Pulse (BVP): Sensor: Thought Technologies SA9308M. Sampling rate: 256 Hz.
Respiration: Sensor: Thought Technologies SA9311M.. Sampling rate: 32 Hz.

## Slide 4
3
Dataset Collection till Now
1. CCUHR (Full)
2. COHFACE (Full)
3. PURE (Full)
4. SCAMPs (Synthetic Data, Full - Downloading in process)
5. UBFC (Full)
6. UBFC-PHYS (20 subjects, Full dataset is too large for storing (754 GB in zip) )

## Slide 5
4
Phase Lag Analysis for CHROM

## Slide 6
5
Need Solid Evidence in Existing Work
Two Types of Lag in Literature:
Constant Lag Study 1 [1] (main paper of CHROM) In Section III, they describe computing color signal standard deviations over sliding temporal windows (1.6–2 s). Because these are effectively linear phase FIR filters (moving averages), they introduce a constant group delay = (N−1)/2 samples. That’s the mathematical basis of the constant lag in CHROM. Study 2 [2] A linear-phase FIR filter introduces a constant group delay equal to (N−1)/2 samples. This applies directly because CHROM’s moving-average over a fixed temporal window is exactly a linear-phase FIR.
Calculation Ref:
1. de Haan, G., & Jeanne, V. (2013). Robust pulse-rate from chrominance-based rPPG. IEEE Transactions on Biomedical Engineering, 60(10), 2878–2886.DOI: 10.1109/TBME.2013.2266196 [link]
2. Oppenheim, A.V., & Schafer, R.W. (2010). Discrete-Time Signal Processing (3rd ed.). Pearson.2. Lyons, Understanding Digital Signal Processing (3rd ed.)

## Slide 7
6
Need Solid Evidence in Existing Work
Two Types of Lag in Literature:
2. FPS lag (drift)
  Study 1 [1] (main paper of CHROM) In this Study: Nominal frame rates may differ from actual effective frame rates, introducing temporal misalignment between ground truth and video-derived signals. This applies to all rPPG algorithms (CHROM, POS, ICA,): a drift between ground truth BVP (60 Hz) and video stream (~29.85 fps vs 30 fps) will accumulate as phase lag. Study 2 [2] AVI files often store only a nominal frame rate (30 fps). The true timestamps may deviate, leading to cumulative drift between streams. This proves that even if CHROM is applied, the video frames are not exactly 30 fps, so the reconstructed signal drifts relative to 60 Hz ground truth.
Calculation Ref:
1. McDuff, D., Estepp, J. R., Piasecki, A. M., & Blackford, E. B. (2015). A survey of remote optical PPG. Proc. IEEE, 103(5), 1207–1225.[link]
2. FFmpeg Documentation – Video Synchronization

## Slide 8
7
Mathematical Analysis of Phase Lag for Subject 09-01.avi
Constant Lag
Observed Initial Lag (Full Dataset):
The mean initial lag over all blocks in the dataset is:
Mean Initial Lag = −8.81frames.
2. Theoretical Constant Lag (from FIR Windowing):
From CHROM's windowing (linear-phase FIR filter with window size N=21):
Constant Lag (theoretical) = (21−1​)\2 = 10 frames.
3. Comparison of Observed and Theoretical Lag: Theoretical constant lag = 10 frames Observed constant lag (mean from full dataset) = −8.81 frames.

## Slide 9
8
Mathematical Analysis of Phase Lag for Subject 09-01.avi
Nominal fps: fv = 30.000 fps
Blocks: 𝑁 = 58
Stride: 𝑇s = 1 s
Data: lag values 𝐿k (frames) at block indices k=0,1,…,57
Time axis: tk = k. Ts
Linear regression model
L(t) ≈ a + bt
Intercept a: constant offset at t=0. Slope b: change in lag (frames) per second.
True fps: ftrue = fv + b
Start offset: t0 = a/ftrue
After Calculations a = −4.8212 frames
b = −0.1388frames/s
R2 = 0.954 (very good fit)
95% CI for slope: [−0.1469,−0.1306].

## Slide 10
9
Mathematical Analysis of Phase Lag for Subject 09-01.avi [cont.]
Applying Formula
True fps: ftrue = fv + b
= 30 + (−0.1388)
= 29.8612 fps
From the MUNet we got the true fps = 29.84 fps
Calculation Ref: 1. Oppenheim, A.V., & Schafer, R.W. (2010). Discrete-Time Signal Processing (3rd ed.). Pearson.2. Lyons, Understanding Digital Signal Processing (3rd ed.), Section 4.6:
2. Pilz, C.-S., Zaunseder, S., Krajewski, J., & Blazek, V. (2018). Local group invariance for heart rate estimation from face videos in the wild. Biomedical Engineering Online, 17(1), 45. [link]
3. Chen, W., & McDuff, D. (2020). DeepPhys++: Reproducing and Benchmarking Remote PPG Methods. Biomedical Optics Express, 11(3), 1268–1283.[link]

## Slide 11
10
Phase Lag Analysis for CHROM For UBFC(36)
After Calculations a = -0.848 frames
b = −0.087 frames/s
R2 = 0.924 (very good fit)
True fps: ftrue = fv + b
= 30 + (−0.087)
= 29.913 fps
Verified fps: 29.90 fps

## Slide 12
11
Phase Lag Analysis for CHROM For UBFC(36)
Constant Lag
Observed Initial Lag (Full Dataset):
The mean initial lag over all blocks in the dataset is:
Mean Initial Lag = −3.46frames.
2. Theoretical Constant Lag (from FIR Windowing):
From CHROM's windowing (linear-phase FIR filter with window size N=21):
Constant Lag (theoretical) = (21−1​)\2 = 10 frames.
3. Comparison of Observed and Theoretical Lag: Theoretical constant lag = 10 frames Observed constant lag (mean from full dataset) = −8.81 frames.

## Slide 13
12
Experimenting With the SCAMPS
SCAMPS dataset contain .mat file which contains: Frame data: RawFrames Xsub Label / physiological signals: d_ppg (photoplethysmogram – PPG) d_br (breathing rate or respiration) d_ekg (ECG / electrocardiogram) d_pitch, d_roll, d_yaw (head pose / orientation) Facial action units: au2, au4, au7, au12, au15, au17, au18, au26, au27, au45 Masks: combined_mask numerical_mask skin_mask
The Full Dataset could not be unzipped because of due to storage shortages.
For experiment the small example of 10 videos and labels (.mat format - 1.2GB) was used.
pyVHR does not support the SCAMPS dataset.
rPPG toolbox supports SCAMPS but does not support Media Pipe land marks, uses the full face detection rectangle.

## Slide 14
13
Experimenting With the SCAMPS
It is important to check if Media Pipe can ditect the synthetic video face landmarks.

## Slide 15
14
Experimenting With the SCAMPS
pyVHR does not support the SCAMPS dataset. So we can not use Mediapipe landmarks for extracting the rgb mean.
But it important to experiment with SCAMPS with the pyVHR/Media Pipe cause most of our excellent results came out from this setup.
So I followed some steps
Convert all raw R G B frames to a single video.
Check Media pipe can recognize the face and detect the landmarks.
Considering the Ground_Truth as 300Hz (as in documentation), Retrieve the ppg, respiration, and timestamp to match the ground_truth as UBFC dataset so that we can use the same pipeline in pyVHR.
We are expecting that CHROM VS Ground Truth should not have any lags or zero lags.