## Slide 1
Rafsan Jany
Korean Convergence Medical Science
Phase Lag Experiment
Breaking Down rPPG-ToolBox

## Slide 2
1
Phase Lag: Biological Impact
Conventional pulse transit times as markers of blood pressure changes in humans [LINK]
The paper evaluates how well different conventional pulse transit times (cPTTs) correlate
with blood pressure (BP) changes in humans. These cPTTs include pulse arrival times (PATs) and
differences between PTTs (dPTTs) derived from ECG and PPG signals at the ear, finger, and toe.

## Slide 3
2
Phase Lag: Biological Impact
Parameter | Correlation with Systolic BP | Practicality | Comment
Toe PAT (foot) | −0.63 ± 0.05 | Low | Best performance, but hard to implement
Finger PAT (foot) | −0.41 ± 0.06 | High | Common, but less reliable
Ear PAT / dPTTs | < 0.3 | Moderate | Weak or inconsistent
Peak-based measures | < 0.3 | — | Much poorer correlation

## Slide 4
3
Phase Lag: Biological Impact
Moens-Korteweg Theory
Pulse wave velocity (PWV) -> how fast the pressure wave travels
along the artery:
Site (superficial veins) | Radius (r) (mm) | Wall thickness (h) (mm) | Elastic modulus (E) (MPa) | PWV (c) (m/s) | Reference
Fingertip veins (central digital veins) | ≈ 0.25 | ≈ 0.08-0.15 (estimate) | ≈ 0.10-0.60 (venous range) | ≈ 3.9-13.0 | Lhuaire M et al., Venous system mapping of the digits and the hand (2022) (PMC)
Forehead veins (supratrochlear / supraorbital / angular) | ≈ 1.0-1.4 | ≈ 0.3-0.5 (estimate) | ≈ 0.10-0.60 | ≈ 3.2-11.9 | Siwetz M et al., The Course and Relation of the Facial Vein in the Face (2023) (MDPI)
Cheek veins (facial vein) | ≈ 0.6-2.25 | ≈ 0.3-0.5 (estimate) | ≈ 0.10-0.60 | ≈ 2.5-15.4 | Pistoia F et al., High-resolution US of the facial vessels (2023) (eurradiolexp.springeropen.com)
𝐸inc = elastic (Young’s) modulus of the arterial wall
ℎ = wall thickness
𝑟 = internal radius of the artery
𝜌 = blood density

## Slide 5
4
Phase Lag: iPPG vs Doppler Sensore
Analysis of Pulse Transit Time Derived from Imaging Photoplethysmography and
Microwave Sensor-based Ballistocardiography [LINK]
The paper proposes a non-contact PTT measurement system using a 24.15 GHz microwave Doppler
sensor for ballistocardiography (BCG) and a camera for imaging PPG (iPPG), synchronized to derive
pulse transit time (PTT). On 16 elderly subjects (69–79 y), noncontact PTT correlated with systolic BP at r = −0.64 (P < 0.05) while PAT (ECG→PPG) correlated only r = −0.20, suggesting PEP confounds PAT.

## Slide 6
5
Phase Lag: Hardware Level
Analysis of Pulse Transit Time Derived from Imaging Photoplethysmography and
Microwave Sensor-based Ballistocardiography [LINK]

## Slide 7
6
Phase Lag Analysis with Python x Biological
RAW Green vs GT BVP
The Preprocess steps of PURE dataset was followed by the rPPG-ToolBox.
RAW green vs GT: lag=-6.58 frames (-219.5 ms)
Path | Distance | PTT @ 6 m/s | PTT range @ 4–8 m/s
Heart → Face | 0.30 m | 0.050 s (50 ms) | 38–75 ms
Heart → Finger | 1.20 m | 0.200 s (200 ms) | 150–300 ms
RAW Calculation from Biological Explanation

## Slide 8
7
Phase Lag Analysis For “ROI”
Root causes inside the ROI:
Spatial phase variation across face Blood-flow timing isn’t uniform. Empirical data show:
    Forehead and cheeks often lead the chin and
    perioral area by ~50–150 ms.
    Motion and lighting can invert phase in some patches.
  When we combine pixels from all of these, we average vectors pointing in different directions on the
  phase circle → the resultant vector’s angle (phase) shifts. If we denote each local pixel’s signal as si​(t)=Ai​cos(ωt+ϕi​),
  then the ROI mean is = 1/N*(Ai​cos(ωt+ϕi​))
  Here Mean(ϕ) ≠ ϕi
(b) Static rectangular box ≠ skin region
  Haar cascade gave a bounding box [236, 123, 483, 370]
  That includes:
    Eyes, lips, hair, background, and moving edges.
    Shadows that change with expression or motion.
  Each non-skin pixel injects luminance-driven noise that lags actual blood-flow modulations
  (illumination fluctuations are slower).
  That drags the average phase toward the illumination signal, not the pulse.
Tiles valid: 64/64
Lag stats — frames: mean +2.14, median -2.98, [-7.74, +15.62]
Lag stats — ms: mean +71.5, median -99.4, [-258.0, +520.6]

## Slide 9
8
Phase Lag Analysis For Demean/Zero-Phase Bandpass Filter (used in rPPG-ToolBox)
Demean only subtracts a constant (the average level).
Subtracting a constant does not shift a waveform in time
Cross-correlation lag is invariant to additive DC and global scaling.
(b) Zero-phase bandpass (butter(...); filtfilt(...)) removes out-of-band content without adding phase delay.
filtfilt applies the filter forward and then backward, cancelling the filter’s phase.
Net phase ≈ 0 ⇒ no group delay ⇒ peak timings preserved (apart from tiny edge effects).
ROI green vs GT: lag=+15.00 fr (+500.0 ms),
xcorr=23.798, box=[236, 123, 483, 370]
Demean ROI green vs GT: lag=+15.00 fr (+500.0 ms), xcorr=23.798
Zero-phase BP vs GT: lag=+15.00 fr (+500.0 ms), xcorr=80.058

## Slide 10
9
Phase Lag Analysis For CHROM/POS
CHROM/POS reduce the lag
ROI mean mixes many effects -> the true pulsatile component (cardiac), -> illumination changes (global brightness/shadows), -> motion/speculars/non-skin leakage.
CHROM and POS are chrominance projections -> cancel common-mode luminance (components along [1,1,1]), -> emphasize color differences that the pulse actually modulates (oxy/deoxy absorption).
Local mean-normalization + energy balancing (α) The per-window normalization and α-scaling equalize the variance of the intermediate channels so illumination drift doesn’t dominate. That reduces phase bias introduced by non-pulsatile terms.
Result With nuisance components reduced, the remaining signal’s phase is closer to the cardiac phase, so the lag shrinks. CHROM (no window): +2.53 fr (~84 ms) POS (no window): +1.66 fr (~55 ms) (vs ROI green’s +15 fr).
CHROM (windowed) vs GT: lag=+3.81 fr (+127.1 ms), xcorr=134.808
POS(windowed) vs GT: lag=+3.53 fr (+117.8 ms), xcorr=86.457

## Slide 11
10
Phase Lag Analysis For CHROM/POS
CHROM/POS For Complete Vedio:
Method | Median Lag (frames) | Std (frames) | Interpretation
CHROM | +0.04 | ±2.89 | Very stable, almost zero-mean phase difference across clips
POS | −0.11 | ±12.24 | Large variability, alternating lead/lag across clips
Study | Reported finding
Wang et al., IEEE TBME 2017 | CHROM shows lower phase error but lower SNR than POS in non-motion cases
Spetlik et al., Sensors 2020 | POS can produce sign-reversed phase during sudden illumination changes
Pilz et al., Front. Physiol. 2022 | POS lag SD ≈ 0.12 s, CHROM lag SD ≈ 0.04 s
Rouast et al., IEEE Access 2023 | “CHROM provides more temporally consistent waveforms; POS improves amplitude under motion but with higher phase drift.”

## Slide 12
11
Phase Lag Analysis For: Video 01-02, 01-03, 01-04, 01-05, 01-06
CHROM median=+0.12 fr ±6.46
POS median=+2.67 fr ±11.57
CHROM median=-0.94 fr ±3.46
POS median=-0.28 fr ±11.10
CHROM median=-0.90 fr ±2.11
POS median=-0.28 fr ±11.2
CHROM median=+0.47 fr ±1.67
POS median=+1.64 fr ±5.66
CHROM median=+0.98 fr ±0.95
POS median=+1.29 fr ±11.29

## Slide 13
12
Appendix
Abbreviation | Full Form | Meaning / Description | Context in Discussion
BCG | Ballistocardiography | Measurement of tiny body movements caused by cardiac ejection of blood (mechanical action of the heart). | Used as the start reference signal in Yoshioka et al. (2020) via 24 GHz radar to compute PTT.
PPG | Photoplethysmography | Optical measurement of blood volume changes in tissue using a light source and detector (usually contact-based). | Conventional contact sensor reference for pulse arrival.
iPPG | Imaging Photoplethysmography | PPG signal extracted from video frames (facial brightness changes), without physical contact. | Used in Yoshioka et al. (2020) for noncontact pulse detection.
rPPG | Remote Photoplethysmography | General term for noncontact PPG obtained from camera images (essentially same as iPPG). | The main signal type in current research focus.
PTT | Pulse Transit Time | Time taken for the arterial pulse wave to travel between two sites (from heart to face). | Key physiological metric; shorter PTT means higher arterial stiffness or BP.
PAT | Pulse Arrival Time | Time between ECG R-wave (electrical heart activation) and PPG pulse arrival; includes pre-ejection period (PEP). | Used in both papers as a surrogate of true PTT.
PEP | Pre-Ejection Period | Time between the ECG R-wave and the actual mechanical ejection of blood from the heart. | Present in PAT, but not in PTT (BCG avoids this).
ECG | Electrocardiography | Electrical recording of heart activity, especially used to detect the R-wave for timing. | Contact reference for PAT in Block et al. (2020).
BP | Blood Pressure | Force exerted by circulating blood on arterial walls. | Physiological parameter correlated inversely with PTT.
SBP | Systolic Blood Pressure | Maximum arterial pressure during heart contraction. | Strongly correlated with PTT (R ≈ −0.6).
DBP | Diastolic Blood Pressure | Minimum arterial pressure during heart relaxation. | Weak correlation with PTT (R ≈ −0.2).
ROI | Region of Interest | Specific area in an image or video used for signal extraction (e.g., cheek or forehead). | In iPPG, face ROI used for green-channel brightness analysis.
FIR | Finite Impulse Response | Type of digital filter used for signal smoothing and noise reduction. | Applied to iPPG signals before peak detection in Yoshioka et al. (2020).
cPTT | Conventional Pulse Transit Time | PTT derived from ECG–PPG or PPG–PPG pairs using contact sensors. | Defined in Block et al. (2020) as traditional, contact-based methods.
dPTT | Differential Pulse Transit Time | Time difference between two distal PPGs (e.g., ear–toe). | Represents the difference of two PTTs, not a true PTT.
PATfoot / PPG foot | — | The waveform onset (foot) used as a reliable timing marker for pulse arrival. | Identified in Block et al. (2020) as more consistent than the peak.