## Slide 1
Rafsan Jany
Korean Convergence Medical Science
Phase Lag Experiment
Breaking Down rPPG-ToolBox

## Slide 2
1
GT Resampler Mechanism from rPPG-toolbox

## Slide 3
2
Phase Lag: Biological Impact
Parameter | Correlation with Systolic BP | Practicality | Comment
Toe PAT (foot) | −0.63 ± 0.05 | Low | Best performance, but hard to implement
Finger PAT (foot) | −0.41 ± 0.06 | High | Common, but less reliable
Ear PAT / dPTTs | < 0.3 | Moderate | Weak or inconsistent
Peak-based measures | < 0.3 | — | Much poorer correlation

## Slide 4
3
Phase Lag: Biological Impact
Moens-Korteweg Theory
Pulse wave velocity (PWV) -> how fast the pressure wave travels
along the artery:
Site (superficial veins) | Radius (r) (mm) | Wall thickness (h) (mm) | Elastic modulus (E) (MPa) | PWV (c) (m/s) | Reference
Fingertip veins (central digital veins) | ≈ 0.25 | ≈ 0.08-0.15 (estimate) | ≈ 0.10-0.60 (venous range) | ≈ 3.9-13.0 | Lhuaire M et al., Venous system mapping of the digits and the hand (2022) (PMC)
Forehead veins (supratrochlear / supraorbital / angular) | ≈ 1.0-1.4 | ≈ 0.3-0.5 (estimate) | ≈ 0.10-0.60 | ≈ 3.2-11.9 | Siwetz M et al., The Course and Relation of the Facial Vein in the Face (2023) (MDPI)
Cheek veins (facial vein) | ≈ 0.6-2.25 | ≈ 0.3-0.5 (estimate) | ≈ 0.10-0.60 | ≈ 2.5-15.4 | Pistoia F et al., High-resolution US of the facial vessels (2023) (eurradiolexp.springeropen.com)
𝐸inc = elastic (Young’s) modulus of the arterial wall
ℎ = wall thickness
𝑟 = internal radius of the artery
𝜌 = blood density

## Slide 5
4
Phase Lag: iPPG vs Doppler Sensore
Analysis of Pulse Transit Time Derived from Imaging Photoplethysmography and
Microwave Sensor-based Ballistocardiography [LINK]
The paper proposes a non-contact PTT measurement system using a 24.15 GHz microwave Doppler
sensor for ballistocardiography (BCG) and a camera for imaging PPG (iPPG), synchronized to derive
pulse transit time (PTT). On 16 elderly subjects (69–79 y), noncontact PTT correlated with systolic BP at r = −0.64 (P < 0.05) while PAT (ECG→PPG) correlated only r = −0.20, suggesting PEP confounds PAT.

## Slide 6
5
Phase Lag: Hardware Level
Analysis of Pulse Transit Time Derived from Imaging Photoplethysmography and
Microwave Sensor-based Ballistocardiography [LINK]

## Slide 7
6
Phase Lag Analysis with Python x Biological
RAW Green vs GT BVP
The Preprocess steps of PURE dataset was followed by the rPPG-ToolBox.
RAW green vs GT: lag=-6.58 frames (-219.5 ms)
Path | Distance | PTT @ 6 m/s | PTT range @ 4–8 m/s
Heart → Face | 0.30 m | 0.050 s (50 ms) | 38–75 ms
Heart → Finger | 1.20 m | 0.200 s (200 ms) | 150–300 ms
RAW Calculation from Biological Explanation

## Slide 8
7
Phase Lag Analysis For “ROI”
Root causes inside the ROI:
Spatial phase variation across face Blood-flow timing isn’t uniform. Empirical data show:
    Forehead and cheeks often lead the chin and
    perioral area by ~50–150 ms.
    Motion and lighting can invert phase in some patches.
  When we combine pixels from all of these, we average vectors pointing in different directions on the
  phase circle → the resultant vector’s angle (phase) shifts. If we denote each local pixel’s signal as si​(t)=Ai​cos(ωt+ϕi​),
  then the ROI mean is = 1/N*(Ai​cos(ωt+ϕi​))
  Here Mean(ϕ) ≠ ϕi
(b) Static rectangular box ≠ skin region
  Haar cascade gave a bounding box [236, 123, 483, 370]
  That includes:
    Eyes, lips, hair, background, and moving edges.
    Shadows that change with expression or motion.
  Each non-skin pixel injects luminance-driven noise that lags actual blood-flow modulations
  (illumination fluctuations are slower).
  That drags the average phase toward the illumination signal, not the pulse.
Tiles valid: 64/64
Lag stats — frames: mean +2.14, median -2.98, [-7.74, +15.62]
Lag stats — ms: mean +71.5, median -99.4, [-258.0, +520.6]

## Slide 9
8
Phase Lag Analysis For Demean/Zero-Phase Bandpass Filter (used in rPPG-ToolBox)
Demean only subtracts a constant (the average level).
Subtracting a constant does not shift a waveform in time
Cross-correlation lag is invariant to additive DC and global scaling.
(b) Zero-phase bandpass (butter(...); filtfilt(...)) removes out-of-band content without adding phase delay.
filtfilt applies the filter forward and then backward, cancelling the filter’s phase.
Net phase ≈ 0 ⇒ no group delay ⇒ peak timings preserved (apart from tiny edge effects).
ROI green vs GT: lag=+15.00 fr (+500.0 ms),
xcorr=23.798, box=[236, 123, 483, 370]
Demean ROI green vs GT: lag=+15.00 fr (+500.0 ms), xcorr=23.798
Zero-phase BP vs GT: lag=+15.00 fr (+500.0 ms), xcorr=80.058

## Slide 10
9
Phase Lag Analysis For CHROM/POS
CHROM/POS reduce the lag
ROI mean mixes many effects -> the true pulsatile component (cardiac), -> illumination changes (global brightness/shadows), -> motion/speculars/non-skin leakage.
CHROM and POS are chrominance projections -> cancel common-mode luminance (components along [1,1,1]), -> emphasize color differences that the pulse actually modulates (oxy/deoxy absorption).
Local mean-normalization + energy balancing (α) The per-window normalization and α-scaling equalize the variance of the intermediate channels so illumination drift doesn’t dominate. That reduces phase bias introduced by non-pulsatile terms.
Result With nuisance components reduced, the remaining signal’s phase is closer to the cardiac phase, so the lag shrinks. CHROM (no window): +2.53 fr (~84 ms) POS (no window): +1.66 fr (~55 ms) (vs ROI green’s +15 fr).
CHROM (windowed) vs GT: lag=+3.81 fr (+127.1 ms), xcorr=134.808
POS(windowed) vs GT: lag=+3.53 fr (+117.8 ms), xcorr=86.457

## Slide 11
10
Phase Lag Analysis For CHROM/POS
CHROM/POS For Complete Vedio:
Method | Median Lag (frames) | Std (frames) | Interpretation
CHROM | +0.04 | ±2.89 | Very stable, almost zero-mean phase difference across clips
POS | −0.11 | ±12.24 | Large variability, alternating lead/lag across clips
Study | Reported finding
Wang et al., IEEE TBME 2017 | CHROM shows lower phase error but lower SNR than POS in non-motion cases
Spetlik et al., Sensors 2020 | POS can produce sign-reversed phase during sudden illumination changes
Pilz et al., Front. Physiol. 2022 | POS lag SD ≈ 0.12 s, CHROM lag SD ≈ 0.04 s
Rouast et al., IEEE Access 2023 | “CHROM provides more temporally consistent waveforms; POS improves amplitude under motion but with higher phase drift.”

## Slide 12
11
Phase Lag Analysis For: Video 01-02, 01-03, 01-04, 01-05, 01-06
CHROM median=+0.12 fr ±6.46
POS median=+2.67 fr ±11.57
CHROM median=-0.94 fr ±3.46
POS median=-0.28 fr ±11.10
CHROM median=-0.90 fr ±2.11
POS median=-0.28 fr ±11.2
CHROM median=+0.47 fr ±1.67
POS median=+1.64 fr ±5.66
CHROM median=+0.98 fr ±0.95
POS median=+1.29 fr ±11.29

## Slide 13
12
Appendix
Abbreviation | Full Form | Meaning / Description | Context in Discussion
BCG | Ballistocardiography | Measurement of tiny body movements caused by cardiac ejection of blood (mechanical action of the heart). | Used as the start reference signal in Yoshioka et al. (2020) via 24 GHz radar to compute PTT.
PPG | Photoplethysmography | Optical measurement of blood volume changes in tissue using a light source and detector (usually contact-based). | Conventional contact sensor reference for pulse arrival.
iPPG | Imaging Photoplethysmography | PPG signal extracted from video frames (facial brightness changes), without physical contact. | Used in Yoshioka et al. (2020) for noncontact pulse detection.
rPPG | Remote Photoplethysmography | General term for noncontact PPG obtained from camera images (essentially same as iPPG). | The main signal type in current research focus.
PTT | Pulse Transit Time | Time taken for the arterial pulse wave to travel between two sites (from heart to face). | Key physiological metric; shorter PTT means higher arterial stiffness or BP.
PAT | Pulse Arrival Time | Time between ECG R-wave (electrical heart activation) and PPG pulse arrival; includes pre-ejection period (PEP). | Used in both papers as a surrogate of true PTT.
PEP | Pre-Ejection Period | Time between the ECG R-wave and the actual mechanical ejection of blood from the heart. | Present in PAT, but not in PTT (BCG avoids this).
ECG | Electrocardiography | Electrical recording of heart activity, especially used to detect the R-wave for timing. | Contact reference for PAT in Block et al. (2020).
BP | Blood Pressure | Force exerted by circulating blood on arterial walls. | Physiological parameter correlated inversely with PTT.
SBP | Systolic Blood Pressure | Maximum arterial pressure during heart contraction. | Strongly correlated with PTT (R ≈ −0.6).
DBP | Diastolic Blood Pressure | Minimum arterial pressure during heart relaxation. | Weak correlation with PTT (R ≈ −0.2).
ROI | Region of Interest | Specific area in an image or video used for signal extraction (e.g., cheek or forehead). | In iPPG, face ROI used for green-channel brightness analysis.
FIR | Finite Impulse Response | Type of digital filter used for signal smoothing and noise reduction. | Applied to iPPG signals before peak detection in Yoshioka et al. (2020).
cPTT | Conventional Pulse Transit Time | PTT derived from ECG–PPG or PPG–PPG pairs using contact sensors. | Defined in Block et al. (2020) as traditional, contact-based methods.
dPTT | Differential Pulse Transit Time | Time difference between two distal PPGs (e.g., ear–toe). | Represents the difference of two PTTs, not a true PTT.
PATfoot / PPG foot | — | The waveform onset (foot) used as a reliable timing marker for pulse arrival. | Identified in Block et al. (2020) as more consistent than the peak.