## Slide 1
Rafsan Jany
Korean Convergence Medical Science
Phase Lag Experiment with toolbox and Raw Code

## Slide 2
1
Verify JSON structure and timing for one PURE sequence
PURE Dataset
(JSON + PNG)
Step 1: JSON Validation
Parse and verify PPG + timestamp integrity
Step 2: Signal Extraction
Extract PPG waveform and video frame times
Step 3: Frame–Time Mapping
Match image filenames to JSON timestamps
Confirm 1:1 mapping between frames & JSON
Step 4: Timestamp Verification
Compare PPG vs frame timestamps
Visualize drift and consistency
Step 5: Alignment & Drift Check
Align PPG and RGB-derived signals
Analyze without manual correction
Step 6: Sliding-Window Lag Analysis
8 s window, 1 s stride
Compute lag (POS / CHROM) per window
Visualize lag trends (line, bar, box)
Step 7: Single-Window Inspection
Select specific window
Plot GT vs rPPG (pointwise differences)
Step 8: Full-Dataset Evaluation
Run on all PURE sequences
Aggregate mean & std lag per subject

## Slide 3
2
Verify JSON structure and timing for one PURE sequence
--- First PPG samples (time_s, waveform, HR_dev_BPM) ---
PPG[ 0] t = 0.0039 s wave = 48 HR = 83 BPM
PPG[ 1] t = 0.0360 s wave = 49 HR = 83 BPM
PPG[ 2] t = 0.0519 s wave = 49 HR = 83 BPM
PPG[ 3] t = 0.0679 s wave = 49 HR = 83 BPM
PPG[ 4] t = 0.0839 s wave = 49 HR = 83 BPM
PPG[ 5] t = 0.0999 s wave = 49 HR = 83 BPM
PPG[ 6] t = 0.1160 s wave = 48 HR = 83 BPM
PPG[ 7] t = 0.1320 s wave = 47 HR = 83 BPM
PPG[ 8] t = 0.1479 s wave = 45 HR = 83 BPM
PPG[ 9] t = 0.1639 s wave = 43 HR = 83 BPM
PPG[ 10] t = 0.1800 s wave = 41 HR = 83 BPM
PPG[ 11] t = 0.1962 s wave = 40 HR = 83 BPM
PPG[ 12] t = 0.2280 s wave = 39 HR = 83 BPM
PPG[ 13] t = 0.2439 s wave = 37 HR = 83 BPM
PPG[ 14] t = 0.2599 s wave = 36 HR = 83 BPM
PPG[ 15] t = 0.2760 s wave = 34 HR = 83 BPM
PPG[ 16] t = 0.2919 s wave = 33 HR = 83 BPM
PPG[ 17] t = 0.3079 s wave = 33 HR = 83 BPM
PPG[ 18] t = 0.3240 s wave = 32 HR = 83 BPM
PPG[ 19] t = 0.3399 s wave = 32 HR = 83 BPM
--- First video frames (time_s) ---
VID[ 0] t = 0.0000 s
VID[ 1] t = 0.0333 s
VID[ 2] t = 0.0667 s
VID[ 3] t = 0.1000 s
VID[ 4] t = 0.1333 s
VID[ 5] t = 0.1667 s
VID[ 6] t = 0.2000 s
VID[ 7] t = 0.2334 s
VID[ 8] t = 0.2667 s
VID[ 9] t = 0.3000 s
VID[ 10] t = 0.3334 s
VID[ 11] t = 0.3667 s
VID[ 12] t = 0.4000 s
VID[ 13] t = 0.4334 s
VID[ 14] t = 0.4667 s
VID[ 15] t = 0.5000 s
VID[ 16] t = 0.5334 s
VID[ 17] t = 0.5667 s
VID[ 18] t = 0.6000 s
VID[ 19] t = 0.6334 s
Video No: 01-01
PPG samples: 4018
Video frames: 2026
--- Sampling statistics ---
PPG fs (mean): 59.340 Hz
PPG fs (std): 6.957 Hz
Video fps (mean): 29.911 Hz
Video fps (std): 0.769 Hz

## Slide 4
3
Verify JSON structure and timing for one PURE sequence
--- First PPG samples (time_s, waveform, HR_dev_BPM) ---
PPG[ 0] t = 0.0014 s wave = 47 HR = 84 BPM
PPG[ 1] t = 0.0174 s wave = 48 HR = 84 BPM
PPG[ 2] t = 0.0335 s wave = 49 HR = 84 BPM
PPG[ 3] t = 0.0494 s wave = 48 HR = 84 BPM
PPG[ 4] t = 0.0654 s wave = 46 HR = 84 BPM
PPG[ 5] t = 0.0814 s wave = 43 HR = 84 BPM
PPG[ 6] t = 0.0974 s wave = 40 HR = 84 BPM
PPG[ 7] t = 0.1134 s wave = 37 HR = 84 BPM
PPG[ 8] t = 0.1294 s wave = 34 HR = 84 BPM
PPG[ 9] t = 0.1454 s wave = 32 HR = 84 BPM
PPG[ 10] t = 0.1614 s wave = 29 HR = 84 BPM
PPG[ 11] t = 0.1774 s wave = 28 HR = 84 BPM
PPG[ 12] t = 0.1934 s wave = 26 HR = 84 BPM
PPG[ 13] t = 0.2094 s wave = 25 HR = 84 BPM
PPG[ 14] t = 0.2254 s wave = 23 HR = 84 BPM
PPG[ 15] t = 0.2414 s wave = 22 HR = 84 BPM
PPG[ 16] t = 0.2574 s wave = 21 HR = 84 BPM
PPG[ 17] t = 0.2734 s wave = 21 HR = 84 BPM
PPG[ 18] t = 0.3054 s wave = 20 HR = 84 BPM
PPG[ 19] t = 0.3214 s wave = 19 HR = 84 BPM
--- First video frames (time_s) ---
VID[ 0] t = 0.0000 s
VID[ 1] t = 0.0333 s
VID[ 2] t = 0.0667 s
VID[ 3] t = 0.1000 s
VID[ 4] t = 0.1333 s
VID[ 5] t = 0.1667 s
VID[ 6] t = 0.2000 s
VID[ 7] t = 0.2334 s
VID[ 8] t = 0.2667 s
VID[ 9] t = 0.3000 s
VID[ 10] t = 0.3334 s
VID[ 11] t = 0.3667 s
VID[ 12] t = 0.4000 s
VID[ 13] t = 0.4334 s
VID[ 14] t = 0.4667 s
VID[ 15] t = 0.5000 s
VID[ 16] t = 0.5334 s
VID[ 17] t = 0.5667 s
VID[ 18] t = 0.6000 s
VID[ 19] t = 0.6334 s
Video No: 01-02
PPG samples: 4002
Video frames: 2023
--- Sampling statistics ---
PPG fs (mean): 59.200 Hz
PPG fs (std): 6.975 Hz
Video fps (mean): 29.911 Hz
Video fps (std): 0.786 Hz

## Slide 5
4
Align PPG to video frame times and visualize from JSON File
Video: 01-01
PPG aligned to frame times using
linear interpolation.
Interpolates (aligns) the 60 Hz PPG
signal to the exact times
of the 30 Hz video frames.
Total PPG samples (raw): 4018
Total frames (aligned points): 2026
Selected window: 5.0 s to 11.0 s
(6.0 s duration)
PPG samples in window: 359
Frames in window: 180
First few aligned frame samples in the
selected window:
t_frame_s PPG_interp_at_frame
0 5.000011 45.491752
1 5.033355 42.323373
2 5.066669 39.579645
3 5.100013 36.495439
4 5.133358 33.411985
5 5.166672 31.664792
6 5.200016 30.245736
7 5.233360 28.173803
8 5.266674 26.080075
9 5.300018 25.000000

## Slide 6
5
Video: 01-01
JSON /Image entries (video frames): 2026
PNG frame files (Image*.png): 2026
Frame counts match.
--- Timestamp comparison ---
Same shape: True
Same values: True
First 10 frame timestamps (JSON vs filename):
[ 0] JSON: 1392643993642815000 IMG: 1392643993642815000 (Image1392643993642815000.png) diff = 0
[ 1] JSON: 1392643993676160000 IMG: 1392643993676160000 (Image1392643993676160000.png) diff = 0
[ 2] JSON: 1392643993709504000 IMG: 1392643993709504000 (Image1392643993709504000.png) diff = 0
[ 3] JSON: 1392643993742818000 IMG: 1392643993742818000 (Image1392643993742818000.png) diff = 0
[ 4] JSON: 1392643993776162000 IMG: 1392643993776162000 (Image1392643993776162000.png) diff = 0
[ 5] JSON: 1392643993809507000 IMG: 1392643993809507000 (Image1392643993809507000.png) diff = 0
[ 6] JSON: 1392643993842821000 IMG: 1392643993842821000 (Image1392643993842821000.png) diff = 0
[ 7] JSON: 1392643993876165000 IMG: 1392643993876165000 (Image1392643993876165000.png) diff = 0
[ 8] JSON: 1392643993909509000 IMG: 1392643993909509000 (Image1392643993909509000.png) diff = 0
[ 9] JSON: 1392643993942823000 IMG: 1392643993942823000 (Image1392643993942823000.png) diff = 0
Result: JSON /Image timestamps and Image*.png filenames match exactly.
This confirms the 1:1 mapping between JSON frames and PNG frames.
Check Image Filenames vs JSON Timestamps

## Slide 7
6
Video: 01-01
JSON /Image entries: 2026
Image*.png frame files: 2026
--- JSON vs filename timestamp check
Same shape: True
Same values: True
--- Duration and offset summary ---
PPG duration: 67.695 s
Video duration: 67.700 s
Start offset (PPG_start - VID_start): 3.944 ms
End offset (PPG_end - VID_end): -1.309 ms
--- Sampling statistics (recomputed) ---
PPG fs (mean): 59.340 Hz
PPG fs (std): 6.957 Hz
Video fps (mean): 29.911 Hz
Video fps (std): 0.769 Hz
--- Nearest-sample delta statistics ---
Mean(|delta|): 4.344 ms
→ On average, each video frame lies only about 4.3 milliseconds away from the closest PPG sample in time.
Max(|delta|): 34.297 ms
→ In the worst case, a frame is about 34 ms away from its nearest PPG sample.
Zoom window: 5.0 s to 11.0 s (6.0 s duration)
PPG samples in window: 359 (59.34 × 6 ≈ 356)
Frames in window: 180 (29.91 × 6 ≈ 179)
Durations match: PPG and video cover the same ~67.7 s; difference is only 5 ms.
Timing diagnostics between PPG timestamps and image (frame) timestamps in JSON

## Slide 8
7
Video: 01-01
Valid windows: 55
CHROM lags (ms) for first few windows:
Window 0 [5.0, 13.0] s: 33.33 ms
Window 1 [6.0, 14.0] s: 33.33 ms
Window 2 [7.0, 15.0] s: 33.33 ms
Window 3 [8.0, 16.0] s: 33.33 ms
Window 4 [9.0, 17.0] s: 33.33 ms
Window 5 [10.0, 18.0] s: 33.33 ms
Window 6 [11.0, 19.0] s: 33.33 ms
Window 7 [12.0, 20.0] s: 33.33 ms
Window 8 [13.0, 21.0] s: 66.67 ms
Window 9 [14.0, 22.0] s: 33.33 ms
CHROM mean lag: 40.10 ms, std: 13.31 ms
CHROM lag (frames): mean = 1.20, std = 0.40
Sliding-window constant-lag analysis with 8 s windows and 1 s stride.

## Slide 9
8
Video: 01-0
Valid windows: 55
CHROM lags (ms) for first few windows:
Window 0 [5.0, 13.0] s: 33.33 ms
Window 1 [6.0, 14.0] s: 33.33 ms
Window 2 [7.0, 15.0] s: 33.33 ms
Window 3 [8.0, 16.0] s: 33.33 ms
Window 4 [9.0, 17.0] s: 33.33 ms
Window 5 [10.0, 18.0] s: 33.33 ms
Window 6 [11.0, 19.0] s: 33.33 ms
Window 7 [12.0, 20.0] s: 33.33 ms
Window 8 [13.0, 21.0] s: 66.67 ms
Window 9 [14.0, 22.0] s: 33.33 ms
CHROM mean lag: 40.10 ms, std: 13.31 ms
CHROM lag (frames): mean = 1.20, std = 0.40
Inspection on Window 0 and 8

## Slide 10
9
Stable, low-variance sequences
Sliding-window constant-lag analysis with 8 s windows and 1 s stride For PUER
Seq | Mean lag (ms) | Std (ms) | Mean (frames) | Comment
01-01 | 40.1 | 13.3 | 1.2 | Textbook case – perfect sync
03-01 | 92.5 | 14.0 | 2.8 | Consistent offset ≈ 3 frames
09-05 | 60.4 | 15.9 | 1.8 | Excellent consistency
10-03 | 50.6 | 16.7 | 1.5 | Steady and clean
01-04 | 33.3 | ~0 | 1.0 | Ideal reference sequence
Moderate variation sequences
Seq | Mean lag (ms) | Comment
05-01 | 69 ± 104 ms | Slight head movement → periodic lag drift
06-01 | 43 ± 144 ms | Possibly illumination fluctuation
07-06 | 17 ± 406 ms | Mild irregularity → artifact windows
08-02 | 11 ± 281 ms | Drifting light or rotation
High-variance / unstable sequences
Seq | Mean lag (ms) | Interpretation
02-02 | 14.7 ± 313 | Large amplitude jitter → temporal mis-sync
04-04 | –61 ± 557 | Motion blur → cross-correlation flattening
05-04 | 199 ± 983 | Gross misalignment, likely drift
05-06 | 206 ± 916 | Periodic inversion → sign changes
07-02 | 23 ± 811 | Lighting modulation / talking
09-04 | 56 ± 492 | Large drift but same polarity
02-05 | 23 ± 129 | Edge case, moderate stability
Aggregate Statistics
Statistic | ms | frames
Global mean lag | 34.4 ms | ≈ 1.03 frames
Global median lag | 33 ms | ≈ 1 frame
Global std lag | ≈ 240 ms | ≈ 7 frames
Interpretation
~70 % of sequences show consistent sub-frame-level lag variance (< 100 ms).
Mean phase lag ≈ 1 frame ≈ 33 ms — physically reasonable for camera–sensor synchronization.
The Caution: High-variance tails (> 300 ms std) correspond to conditions with motion, lighting flicker, or low SNR.
These distort the cross-correlation, shifting or flattening peaks → apparent phase jumps.

## Slide 11
Raw Code Experiment on UBFC

## Slide 12
11
Raw Code for UBFC
UBFC Dataset
(video.avi + gt.txt)
Step 1: GT.txt Validation
Parse and verify PPG + timestamp integrity
Step 2: Signal Extraction
Extract PPG waveform
Step 3: Frame–Time Mapping
Match GT to timestamps
Confirm 1:1 mapping between GT & timestamps
Step 4: Timestamp Verification
Compare GT vs timestamps
Visualize drift and consistency
Step 5: Alignment & Drift Check
Align PPG and RGB-derived signals
Analyze without manual correction
Step 6: Sliding-Window Lag Analysis
8 s window, 1 s stride
Compute lag (POS / CHROM) per window
Visualize lag trends (line, bar, box)
Step 7: Single-Window Inspection
Select specific window
Plot GT vs rPPG (pointwise differences)
Step 8: Full-Dataset Evaluation
Run on all PURE sequences
Aggregate mean & std lag per subject

## Slide 13
12
Verify gt.txt structure and timing for one UBFC Subject
Check GT and Video timing
Video No: 01
GT loaded successfully: 1547 PPG samples, 1547 timestamps
PPG samples and timestamps are 1:1 aligned (same length)
GT PPG duration: 52.691 s
GT fps:
Video info: 1547 frames @ 29.264 fps → 52.863 s
Duration difference (video − GT): 0.172 s
Problematic Zone:
PPG: 0 → 52.691 s
Video: 0 → 52.863 s
That’s a 0.172 s offset (≈5 frames @ 29.3 fps).
So, even though there are 1547 PPG values and 1547 frames,
the last few video frames occur after the PPG stopped recording.
Visualize GT/Video timing
Loaded GT: 1547 samples
1 duplicated or non-increasing timestamps found at indices [494]
→ Adjusted duplicated timestamps by +1e-6 s increments.
Video info: 1547 frames @ 29.264 fps → 52.863 s
GT PPG duration: 52.691 s
Duration difference (video − GT): 0.172 s ≈ 5.04 frames (0.33 % of duration)
Frames within overlap: 1542 (5 trimmed)

## Slide 14
13
Align GT PPG to video frame times
Loaded raw GT: 1547 PPG samples
--- GT timestamp anomaly report ---
1 non-increasing timestamps corrected at indices: [495]
GT PPG duration: 0.000 s → 52.691 s (Δ=52.691 s)
GT dt stats: min=0.000001 s, max=0.223000 s, mean=0.034082 s
Video info: 1547 frames @ 29.264 fps → 52.863 s (0.000 s → 52.829 s)
--- Overlap between GT and video ---
GT range: [0.000, 52.691] s (duration 52.691 s)
Video range: [0.000, 52.829] s (duration 52.863 s)
Overlap frames: 1542 / 1547 (trim start=0, trim end=5)
Interpolated GT PPG onto 1542 frame timestamps within overlap.
First 10 overlapping frames (frame_idx, t_frame, nearest t_ppg, Δt):
frame 0: t_frame= 0.0000 s, nearest t_ppg= 0.0000 s, Δt= 0.000 ms
frame 1: t_frame= 0.0342 s, nearest t_ppg= 0.0550 s, Δt= -20.828 ms
frame 2: t_frame= 0.0683 s, nearest t_ppg= 0.0670 s, Δt= 1.343 ms
frame 3: t_frame= 0.1025 s, nearest t_ppg= 0.1090 s, Δt= -6.485 ms
frame 4: t_frame= 0.1367 s, nearest t_ppg= 0.1200 s, Δt= 16.686 ms
frame 5: t_frame= 0.1709 s, nearest t_ppg= 0.1730 s, Δt= -2.142 ms
frame 6: t_frame= 0.2050 s, nearest t_ppg= 0.2170 s, Δt= -11.971 ms
frame 7: t_frame= 0.2392 s, nearest t_ppg= 0.2290 s, Δt= 10.201 ms
frame 8: t_frame= 0.2734 s, nearest t_ppg= 0.2710 s, Δt= 2.372 ms
frame 9: t_frame= 0.3075 s, nearest t_ppg= 0.2920 s, Δt= 15.544 ms
Visualization window: [23.329, 29.329] s (≈6.000 s)
GT samples in window: 181, frame-aligned samples in window: 176

## Slide 15
14
Phase Lag Between CHROM and GT
Loaded raw GT: 1547 PPG samples
CHROM lag (ms): mean = 61.51, std = 851.61
CHROM lag (frames): mean = 1.80, std = 24.92
First few windows:
Window 0 [0.0, 8.0] s: 820.12 ms, 24.00 frames
Window 1 [1.0, 9.0] s: -102.51 ms, -3.00 frames
Window 2 [2.0, 10.0] s: -375.89 ms, -11.00 frames
Window 3 [3.0, 11.0] s: -375.89 ms, -11.00 frames
Window 4 [4.0, 12.0] s: 512.57 ms, 15.00 frames
Window 5 [5.0, 13.0] s: 512.57 ms, 15.00 frames
Window 6 [6.0, 14.0] s: -375.89 ms, -11.00 frames
Window 7 [7.0, 15.0] s: -341.72 ms, -10.00 frames
Window 8 [8.0, 16.0] s: -1230.18 ms, -36.00 frames
Window 9 [9.0, 17.0] s: -307.54 ms, -9.00 frame

## Slide 16
rPPG-toolbox Reference Code

## Slide 17
16
GT Downsampled Mechanism from rPPG-toolbox

## Slide 18
17
Mismatch of FPS: Vedio
For We assume that frames are uniformly spaced at the true frame rate:
Our current processing pipeline assumes a fixed 30 fps rate:
For a 6s window, we expect exactly 180 frames:
When we calculate the number of the frame the number of the frame was exactly 180. No missing Frames. But
If the real frame rate is:
Then, The true window duration ≈ 6.02 s
Difference: ≈ 20 ms (video side)

## Slide 19
18
Mismatch of FPS: GT
For the video stream, we do not have per-frame timestamps — only the total duration and number of frames.
For the ground-truth (GT) signal, we have use true timestamps and they are not perfectly uniform.
The average sampling interval is:
For a 6-second window, we expect exactly 180 frames:
An Ideal 60 Hz signal would yield 6 x 60 =360
The true GT signal provides roughly 6 x (59.2Hz – 59.3Hz) = 355-356 sample
hus, we lose around 4–5 samples on average per window
When we later resample the GT signal (such as: 60 → 30 Hz, or directly to frame times), the interpolation
process fills these gaps, yielding one GT value per frame.
Numerically, no values are missing — but physically, the underlying waveform briefly lacks real measurements.

## Slide 20
19
Mismatch of FPS: Synchronization Problem
Video FPS = 30Hz
Ground-truth (GT) sensor sampling rate = 60 Hz
Source | True rate | Assume rate | Difference
Video | 29.9114 Hz | 30 Hz | -0.29% (slightslower)
GT | 59.340 Hz | 60 Hz | -1.10% (slightslower)
Let
Video drift over 6s
GT drift over 6s
Combined mismatch

## Slide 21
20
Mismatch of FPS: Synchronization Problem
Why this occur?
The assumed sampling-rate ration
But true ratio:
This 0.8 % slope error accumulates steadily, producing a linear phase lag between the signals.

## Slide 22
21
Mismatch of FPS: Synchronization Problem
Over All analysis of PURE dataset
Across all 59 recordings, the true GT sampling rate averaged:59.46 Hz ± 0.30 Hz
The video frame rate averaged: 29.97 Hz ± 0.04 Hz

## Slide 23
22
Phase Lag Compensate Literatures - 1
Adaptive compensation of measurement delays in multi-sensor fusion for inertial motion tracking using
moving horizon estimation (2022)
The Problem – Time Misalignment in Multi-Sensor Fusion
Modern motion-tracking systems combine sensors like IMUs (fast) and GNSS (slow).
Each sensor has its own clock, sampling rate, and processing pipeline, leading to:Unknown & varying delays (GNSS data arrives late by 100–200 ms).
Different sampling rates (multi-rate problem).
No common synchronization signal between subsystems.
These delays cause pose estimation drift, since data are fused assuming incorrect timestamps.
→ Even a small delay can introduce centimeter-scale position error or degree-scale orientation error.
The Solution – Adaptive Delay Estimation via MHE + Direct Collocation
The authors reformulate the fusion problem as a continuous-time Moving Horizon Estimation (MHE) optimization.
Instead of assuming fixed sampling times, they: Model system dynamics continuously (IMU motion model).
Use direct collocation – represent the state trajectory by smooth polynomials.
Treat each measurement’s true timestamp (τₖ) as an optimization variable.
Estimate τₖ jointly with states (position, velocity, orientation) to find the best-aligned delay automatically.
This means the estimator adapts to unknown, time-varying delays — no external sync signal needed.
Make the estimator itself “learn” the time delay — by optimizing measurement timing in a continuous-time MHE framework, sensors can stay synchronized without hardware sync lines.

## Slide 24
23
Phase Lag Compensate Literature - 1
Adaptive compensation of measurement delays in multi-sensor fusion for inertial motion tracking using
moving horizon estimation (2022)
Outcome -
Applied to IMU + RTK-GNSS fusion.
Achieved 10× improvement in position/orientation accuracy (≈ 2 cm & < 1°).
Estimated GNSS delay within ≈ 5 ms (sim) and ≈ 50 ms (real).
Horizon length N ≈ 4 balances accuracy vs computational cost.
In remote PPG (rPPG):
The video-based signal (from camera) and the ground-truth contact PPG are often out of phase,
due to:
  1.Camera frame capture latency (≈ 30–200 ms)
  2.Rolling-shutter effects
  3.Processing delays in the rPPG extraction pipeline
Even small phase lags distort waveform alignment and degrade HR/RR estimation.
That’s exactly the same kind of time-delay problem — just in a physiological context instead of IMU/GNSS.

## Slide 25
24
Phase Lag Compensate Literatures - 2
Simultaneous Spatiotemporal Bias Compensation and Data Fusion for Asynchronous Multisensor Systems(2024)
The Core Problem:
In multi-sensor systems (radar, camera, IMU), measurements arrive asynchronously and often
contain two types of bias:
1.Spatial bias: positional misalignment between sensors (angle or range offset)
2.Temporal bias: unknown time delays between a measurement’s timestamp and its true measurement time
Traditional fusion algorithms (Kalman Filter) assume timestamps are accurate.
→ But in real systems, processing and communication latencies make timestamps unreliable.
→ Leads to time misalignment, fusion errors, or even duplicate tracks.
Example:If sensor A’s measurement arrives 200 ms late and sensor B’s 50 ms early,
fusing them naïvely will distort the tracked position or phase
— exactly the same issue as your rPPG vs contact-PPG phase lag.

## Slide 26
25
Phase Lag Compensate Literatures - 2
Simultaneous Spatiotemporal Bias Compensation and Data Fusion for Asynchronous Multisensor Systems(2024)
The Solution –
Step 1 — Augment the State Vector
They define an augmented state:
𝑋(𝑘)=[target state, spatial biases, temporal biases]
so that the temporal bias (time delay) of each sensor becomes part of the variable set estimated by the filter
Step 2 — Build Bias-Aware Equations
They reformulate:
-> The state transition equation (motion model)
-> The measurement equation (what each sensor observes)
to explicitly include delay terms Δ𝑡𝑠, between each sensor 𝑠s and the reference sensor.
This allows the filter to align asynchronous measurements by compensating for their individual delays.
Step 3 — Two Fusion Modes
They propose two complementary algorithms:
Method | Description | Use Case
BP-SBDF (Batch Processing Spatiotemporal Bias & Data Fusion) | Collects measurements over a time window and fuses them together. | When multiple sensors report asynchronously but within a known interval.
SP-SBDF (Sequential Processing …) | Updates as soon as any sensor measurement arrives (real-time). | For streaming, online fusion.

## Slide 27
26
Out Topic: SOLID
Update On Development/Deployment Research Process
S — Single Responsibility Principle (SRP)
A class should have only one reason to change — it should do one thing well.
Example: Separate classes for InvoicePrinter and InvoiceCalculator.
O — Open/Closed Principle (OCP)
Software entities should be open for extension, but closed for modification
Example: Add new shapes to a draw() method using inheritance, not rewriting.
L — Liskov Substitution Principle (LSP)Subtypes must be substitutable for their base types.
Example: A Square class should behave like a Rectangle wherever it’s used.
I — Interface Segregation Principle (ISP)
Clients should not depend on interfaces they do not use.
Example: Split a bulky IWorker interface into IPrinter, IScanner, etc.
D — Dependency Inversion Principle (DIP)Depend on abstractions, not on concrete classes.
Example: Use an ILogger interface instead of directly calling FileLogger.

## Slide 28
27
Appendix
Abbreviation | Full Form | Meaning / Description | Context in Discussion
BCG | Ballistocardiography | Measurement of tiny body movements caused by cardiac ejection of blood (mechanical action of the heart). | Used as the start reference signal in Yoshioka et al. (2020) via 24 GHz radar to compute PTT.
PPG | Photoplethysmography | Optical measurement of blood volume changes in tissue using a light source and detector (usually contact-based). | Conventional contact sensor reference for pulse arrival.
iPPG | Imaging Photoplethysmography | PPG signal extracted from video frames (facial brightness changes), without physical contact. | Used in Yoshioka et al. (2020) for noncontact pulse detection.
rPPG | Remote Photoplethysmography | General term for noncontact PPG obtained from camera images (essentially same as iPPG). | The main signal type in current research focus.
PTT | Pulse Transit Time | Time taken for the arterial pulse wave to travel between two sites (from heart to face). | Key physiological metric; shorter PTT means higher arterial stiffness or BP.
PAT | Pulse Arrival Time | Time between ECG R-wave (electrical heart activation) and PPG pulse arrival; includes pre-ejection period (PEP). | Used in both papers as a surrogate of true PTT.
PEP | Pre-Ejection Period | Time between the ECG R-wave and the actual mechanical ejection of blood from the heart. | Present in PAT, but not in PTT (BCG avoids this).
ECG | Electrocardiography | Electrical recording of heart activity, especially used to detect the R-wave for timing. | Contact reference for PAT in Block et al. (2020).
BP | Blood Pressure | Force exerted by circulating blood on arterial walls. | Physiological parameter correlated inversely with PTT.
SBP | Systolic Blood Pressure | Maximum arterial pressure during heart contraction. | Strongly correlated with PTT (R ≈ −0.6).
DBP | Diastolic Blood Pressure | Minimum arterial pressure during heart relaxation. | Weak correlation with PTT (R ≈ −0.2).
ROI | Region of Interest | Specific area in an image or video used for signal extraction (e.g., cheek or forehead). | In iPPG, face ROI used for green-channel brightness analysis.
FIR | Finite Impulse Response | Type of digital filter used for signal smoothing and noise reduction. | Applied to iPPG signals before peak detection in Yoshioka et al. (2020).
cPTT | Conventional Pulse Transit Time | PTT derived from ECG–PPG or PPG–PPG pairs using contact sensors. | Defined in Block et al. (2020) as traditional, contact-based methods.
dPTT | Differential Pulse Transit Time | Time difference between two distal PPGs (e.g., ear–toe). | Represents the difference of two PTTs, not a true PTT.
PATfoot / PPG foot | — | The waveform onset (foot) used as a reliable timing marker for pulse arrival. | Identified in Block et al. (2020) as more consistent than the peak.