## Slide 1
Applying All The Algorithms to Full Dataset Of UBFC
Finding The Optimum Peak Finding Algorithms
Applying Various Processing Methods with Time Domain
Visually Analysis The frame wise Error
Two Peak Problems
Rafsan Jany
Korean Convergence Medical Science

## Slide 2
3 x
31 x
15 x
Experiment Paths
Sub 1
Sub 2
Sub 3
Sub 4
Sub 5
Sub 46
Sub 47
Sub 48
Sub 49
40
Subjects
Mean RGB
Extraction
All ROI
Only Forehead
Only Both Cheeks
Green
Channel
ICA 1
ICA 2
POS
PCA 2
PCA 3
RED
Channel
Blue
Channel
CHROM
POS++
CHROM
++
PCA 1
Kalman
POS
Kalman
Green
31 Peak Detection Methods
ICA 3
Normal HR
Z Scored Based HR
Threshold based HR
3 x

## Slide 3
Results From Full Dataset + ALL ROI
100 Frames, 3 Sec
Rank | Signal Source | HR Calculation Type | Peak Finding Algorithm | Average MAE
1 | Kalman Green | Threshold filtered | savgol_peak | 13.57
2 | Green_Channel_Signal | Threshold filtered | slope_sum_function | 14.89
3 | Kalman Green | Threshold filtered | slope_sum_function | 14.92
4 | Kalman Green | Threshold filtered | gaussian_smooth_peaks | 15.06
5 | Kalman Green | Threshold filtered | bandpass_local_maxima | 15.20
6 | Green_Channel_Signal | Threshold filtered | median_filtered_peaks | 16.47
7 | Green_Channel_Signal | Threshold filtered | savgol_peak | 16.55
8 | Green_Channel_Signal | Threshold filtered | bandpass_local_maxima | 17.69
9 | Blue Channel | Threshold filtered | slope_sum_function | 18.81
10 | ICA Component 2 | Threshold filtered | slope_sum_function | 19.61

## Slide 4
Results From Full Dataset + ALL ROI
300 Frames, 10 Sec
Rank | Signal Source | HR Calculation Type | Peak Finding Algorithm | Average MAE
1 | Green_Channel_Signal | Threshold filtered | fast_ampd | 8.60
2 | Green_Channel_Signal | Normal | fast_ampd | 8.89
3 | Green_Channel_Signal | Z-score filtered | fast_ampd | 9.24
4 | PCA Component 3 | Threshold filtered | fast_ampd | 9.55
5 | Kalman Green | Threshold filtered | fast_ampd | 9.62
6 | PCA Component 3 | Normal | fast_ampd | 9.68
7 | Kalman Green | Normal | fast_ampd | 9.77
8 | Kalman Green | Z-score filtered | fast_ampd | 10.00
9 | ICA Component 2 | Threshold filtered | fast_ampd | 10.36
10 | ICA Component 2 | Normal | fast_ampd | 10.94

## Slide 5
Results From Full Dataset + Both Cheeks ROI
100 Frames, 3 Sec
Rank | Signal Source | HR Calculation Type | Peak Finding Algorithm | Average MAE
1 | Kalman Green | Threshold filtered | savgol_peak | 13.57
2 | Green_Channel_Signal | Threshold filtered | slope_sum_function | 14.89
3 | Kalman Green | Threshold filtered | slope_sum_function | 14.92
4 | Kalman Green | Threshold filtered | gaussian_smooth_peaks | 15.06
5 | Kalman Green | Threshold filtered | bandpass_local_maxima | 15.20
6 | Green_Channel_Signal | Threshold filtered | median_filtered_peaks | 16.47
7 | Green_Channel_Signal | Threshold filtered | savgol_peak | 16.55
8 | Green_Channel_Signal | Threshold filtered | bandpass_local_maxima | 17.69
9 | Blue Channel | Threshold filtered | slope_sum_function | 18.81
10 | ICA Component 2 | Threshold filtered | slope_sum_function | 19.61

## Slide 6
Results From Full Dataset + Both Cheeks ROI
300 Frames, 10 Sec
Rank | Signal Source | HR Calculation Type | Peak Finding Algorithm | Average MAE
1 | Green_Channel_Signal | Threshold filtered | fast_ampd | 9.66
2 | ICA Component 1 | Threshold filtered | fast_ampd | 9.86
3 | Kalman Green | Threshold filtered | fast_ampd | 9.87
4 | ICA Component 1 | Z-score filtered | fast_ampd | 9.93
5 | Green_Channel_Signal | Normal | fast_ampd | 10.00
6 | Kalman Green | Threshold filtered | median_filtered_peaks | 10.02
7 | Kalman Green | Threshold filtered | sliding_window | 10.08
8 | Green_Channel_Signal | Z-score filtered | fast_ampd | 10.25
9 | Kalman Green | Normal | fast_ampd | 10.27
10 | Kalman Green | Z-score filtered | fast_ampd | 10.50

## Slide 7
Results From Full Dataset + ForeHead ROI
100 Frames, 3 Sec
Rank | Signal Source | HR Calculation Type | Peak Finding Algorithm | Average MAE
1 | Kalman Green | Threshold filtered | slope_sum_function | 19.87
2 | ICA Component 2 | Threshold filtered | median_filtered_peaks | 21.14
3 | PCA Component 2 | Threshold filtered | median_filtered_peaks | 21.47
4 | PCA Component 3 | Threshold filtered | median_filtered_peaks | 21.83
5 | Green_Channel_Signal | Threshold filtered | slope_sum_function | 21.56
6 | PCA Component 2 | Threshold filtered | bandpass_local_maxima | 22.04
7 | PCA Component 3 | Threshold filtered | sliding_window | 22.15
8 | Green_Channel_Signal | Threshold filtered | bandpass_local_maxima | 22.60
9 | Green_Channel_Signal | Threshold filtered | savgol_peak | 22.99
10 | ICA Component 2 | Threshold filtered | slope_sum_function | 23.05

## Slide 8
Results From Full Dataset + ForeHead ROI
300 Frames, 10 Sec
Rank | Signal Source | HR Calculation Type | Peak Finding Algorithm | Average MAE
1 | PCA Component 3 | Threshold filtered | fast_ampd | 10.51
2 | ICA Component 1 | Normal | fast_ampd | 10.53
3 | PCA Component 3 | Normal | fast_ampd | 10.56
4 | ICA Component 1 | Threshold filtered | fast_ampd | 10.60
5 | PCA Component 3 | Z-score filtered | fast_ampd | 10.76
6 | ICA Component 1 | Z-score filtered | fast_ampd | 10.82
7 | ICA Component 2 | Threshold filtered | fast_ampd | 11.92
8 | Green_Channel_Signal | Threshold filtered | fast_ampd | 12.00
9 | PCA Component 2 | Threshold filtered | fast_ampd | 12.01
10 | PCA Component 2 | Normal | fast_ampd | 12.14

## Slide 9
All ROI + 300 Frames
AVG MAE: 8.60

## Slide 10
All ROI + 300 Frames
AVG MAE: 9.55

## Slide 11
All ROI + 300 Frames
AVG MAE: 9.62

## Slide 12
Window Wise Comparison
Peak Detection Algorithm: fast_ampd
Signal Channel: Green
roi_mode = "forehead"
Subject: 1
gt_hr: 98.22667
est_hr: 101.40845070422534

## Slide 13
Window Wise Comparison For Subject 1
gt_hr: 99.2025
est_hr: 101.12359550561797
Peak Detection Algorithm: fast_ampd
Signal Channel: Green
roi_mode = "forehead"
Subject: 1

## Slide 14
Window Wise Comparison For Subject 1
gt_hr: 97.0
est_hr: 97.29729729729729
Peak Detection Algorithm: fast_ampd
Signal Channel: Green
roi_mode = "forehead"
Subject: 1

## Slide 15
Fixing the Peaks
local_maxima: Frames([13, 21, 32, 39, 55, 72, 89])
accepted_peaks: Frames([21, 39, 55, 72, 89])
rejected_peaks: Frames([13, 32])
prominences: 1.085, 0.928, 1.246, 0.594, 0.638

## Slide 16
Fixing the Peaks
Prominence: The vertical distance between the peak and its lowest surrounding valley (left or right) before a higher peak appears.

## Slide 17
Wrapper Algorithm For Fixing the Peak
1. Finding All Local Maxima
2. Comparing Each Pair of Neighboring Peaks
p1, p2 = peaks[i], peaks[i + 1]
3. Checking if These Peaks Are Too Close close = (p2 - p1) < min_distance_frames(10)
4. Checking if Their Heights or Prominences Are Similar similar_prominence = max(prom1, prom2) / min(prom1, prom2) < prominence_ratio_thresh(1.5)
similar_amplitude = abs(amp1 - amp2) < amplitude_diff_thresh(0.2)
5. Finding The Mid: mid = int((p1 + p2) / 2)
All Local Maxima | Fixed Peaks
13 | 13.0
21 | 21.0
32 | 35.0
39 | 55.0
55 | 72.0
72 | 89.0
89 | NaN

## Slide 18
Algorithm For Fixing the Peak
6. Ploting the new Signal (for only visualizations)

## Slide 19
Task Pending
Now Comparision using FFT Vs Current
FFT vs Median
FFT vs Hestoric wrapper…historic is the method to remove the unusual HR from the dataset…