## Slide 1
Rafsan Jany
Korean Convergence Medical Science
Detailed Results Analysis For UBFC AND PURE Dataset
for
pyVHR_X_PEAK Method

## Slide 2
pyVHR Peak Detection Hybrid Experiment
Mean RGB
Extraction
CHROM/POS
Ground Truth
Line 0: [values of the BVP signal]
BVP Signal
Peak Detection
scipy_find_peaks
Tunned
Ampd
Tunned
1
MAE
BPM
Peak-to-Peak Interval
BPM Calculation
Peak Detection Experiments
BVP Signal
pyVHR FrameWork
Find The Median For Each Block
Peak-to-Peak Interval
BPM Calculation
Find The Median For Each Block

## Slide 3
UBFC Dataset Result Summery
2
Method | MAE | Std Dev | Worst Case (Max)
AMPD + CHROM | 2.61 | 1.24 | 5.29
AMPD + POS | 9.59 | 5.06 | 28.54
SciPy + CHROM | 4.39 | 4.38 | 25.06
SciPy + POS | 13.80 | 9.86 | 47.43

## Slide 4
AMPD + CHROM: MAE
3
Method | MAE | Std Dev | Worst Case (Max)
AMPD + CHROM | 2.61 | 1.24 | 5.29

## Slide 5
AMPD + POS: MAE
4
Method | MAE | Std Dev | Worst Case (Max)
AMPD + POS | 9.59 | 5.06 | 28.54

## Slide 6
SciPy + CHROM: MAE
5
Method | MAE | Std Dev | Worst Case (Max)
SciPy + CHROM | 4.39 | 4.38 | 25.06

## Slide 7
SciPy + POS: MAE
6
Method | MAE | Std Dev | Worst Case (Max)
SciPy + POS | 13.80 | 9.86 | 47.43

## Slide 8
UBFC Dataset Result Summery
7

## Slide 9
Tunning Mechanism
8
peaks, properties = find_peaks(signal,
  distance=min_distance,
  prominence=prominence,
  height=height)
After Tunning
Distance = 10,
Prominence = 0.5,
height= Default
[Hard Coded]
ampd(signal: np.ndarray,
L: int = None)
N = Signal Length
L = int(N 2 - 1)
After Tunning
L = 10
[Hard Coded]
Time To apply this in PURE dataset

## Slide 10
PURE Dataset Result Summery: With Tunned ALgo
9
Method | MAE | Std Dev
AMPD + CHROM | 41.99 | 10.57
AMPD + POS | 54.46 | 4.75
SciPy + CHROM | 25.50 | 6.8
SciPy + POS | 51.98 | 21.49
Method | MAE | Std Dev
AMPD + CHROM | 45.24 | 12.41
AMPD + POS | 55.06 | 11.09
SciPy + CHROM | 25.75 | 6.32
SciPy + POS | 43.80 | 24.55
Method | MAE | Std Dev
AMPD + CHROM | 45.89 | 10.35
AMPD + POS | 56.92 | 5.34.
SciPy + CHROM | 24.47 | 4.88
SciPy + POS | 46.93 | 21.80
Method | MAE | Std Dev
AMPD + CHROM | 41.89 | 9.28
AMPD + POS | 50.57 | 7.97
SciPy + CHROM | 24.62 | 5.75
SciPy + POS | 50.13 | 22.96
Method | MAE | Std Dev
AMPD + CHROM | 42.68 | 9.11
AMPD + POS | 50.09 | 6.69
SciPy + CHROM | 25.21 | 4.84
SciPy + POS | 44.91 | 23.05
Method | MAE | Std Dev
AMPD + CHROM | 42.52 | 10.32
AMPD + POS | 54.24 | 5.14
SciPy + CHROM | 24.01 | 5.28
SciPy + POS | 44.70 | 23.43
Steady
Talking
Slow Translation
Fast Translation
Small Rotation
Medium Rotation

## Slide 11
EST VS GT FOR PURE [SciPy(tunned) + CHROM]
10
Steady
Talking
Slow Translation

## Slide 12
Small Rotation
EST VS GT FOR PURE [SciPy(tunned) + CHROM]
11
Fast Translation
Medium Rotation

## Slide 13
Challenges
12
Its Often repeated in Problem Solving World:-
Hard coding is like carving answers in stone,
until it crumbles under pressure.
Signal amplitude varies (due to motion or
lighting changes and FPS).
Noise level changes (different SNR blocks).
Heart rate varies (across individuals or time).
Need Universal Tunning Mechanism
Why Results are so bad?
Motion and lighting changes
Change of FPS 30 to 60.
Different SNR blocks

## Slide 14
Solution
13
1. Physiological Constraint on Peak Distance
This comes from heart rate physiology:
If HR_max = 180 bpm → beats every ~0.33 sec → at 30 fps = 10 frames apart minimum.
Why: Prevents detecting two peaks too close together (false positives from noise).
Reference:J. Pan and W. J. Tompkins, "A Real-Time QRS Detection Algorithm," in IEEE Transactions on Biomedical Engineering, vol. BME-32, no. 3, pp. 230-236, March 1985, doi: 10.1109/TBME.1985.325532.
2. Height Threshold = Mean + α·STD
height=𝜇+𝛼⋅𝜎
Why: In signals where amplitude varies, a static threshold fails.
Using mean + k·std ensures the threshold adapts to:
Higher amplitude → threshold rises → avoids false positives.
Lower amplitude → threshold drops → avoids missed peaks.
Reference: M. Elgendi, "On the Analysis of QRS Detection Algorithms," Sensors, vol. 13, no. 5, pp. 6149–6179, 2013. doi: 10.3390/s130506149
3. Prominence = β·STD
prominence=𝛽⋅𝜎
Prominence ensures the peak stands out relative to neighbors.
Setting it as a fraction of signal variability accounts for noise.
Reference: Scholkmann, F., Boss, J., & Wolf, M. (2012). An Efficient Algorithm for Automatic Peak Detection in Noisy Periodic and Quasi-Periodic Signals. Algorithms, 5(4), 588–603. https://doi.org/10.3390/a5040588

## Slide 15
Adaptive Tunning Mechanism
14
peaks, properties = find_peaks(signal,
  distance=min_distance,
  prominence=prominence,
  height=height)
Adaptive Mechanism
[Adaptive]
ampd(signal: np.ndarray, fps,
L: int = None):
N = Signal Length
L = int(N 2 - 1)
Adaptive Mechanism
[Adaptive]
Signal Amplitude ∝ 𝜎

## Slide 16
PURE Dataset Result Summery Using Adaptive [CHROM]
15
Steady
Talking
Slow Translation
Fast Translation
Small Rotation
Medium Rotation
Method | MAE | Std Dev
AMPD_Adaptive | 24.393252 | 17.985039
Scipy_Adaptive | 2.893107 | 1.760998
Method | MAE | Std Dev
AMPD_Adaptive | 22.956472 | 19.521787
Scipy_Adaptive | 4.918641 | 4.137012
Method | MAE | Std Dev
AMPD_Adaptive | 23.158704 | 15.384304
Scipy_Adaptive | 3.372643 | 2.743749
Method | MAE | Std Dev
AMPD_Adaptive | 19.501936 | 14.680868
Scipy_Adaptive | 2.332530 | 1.432035
Method | MAE | Std Dev
AMPD_Adaptive | 13.714386 | 8.249087
Scipy_Adaptive | 3.113621 | 1.829347
Method | MAE | Std Dev
AMPD_Adaptive | 14.008665 | 5.125412
Scipy_Adaptive | 3.297898 | 1.666147

## Slide 17
EST VS GT FOR PURE [Scipy_Adaptive+ CHROM]
16
Steady
Talking
Slow Translation

## Slide 18
Small Rotation
EST VS GT FOR PURE [Scipy_Adaptive+ CHROM]
17
Fast Translation
Medium Rotation

## Slide 19
Applying Scipy Adaptive on UBFC Dataset
18
Previous
Result
Method | MAE | Std Dev
SciPy + CHROM | 4.39 | 4.38

## Slide 20
UBFC Dataset Result Adaptive [CHROM]
19
Method | MAE | Std Dev
AMPD_Adaptive | 18.082846 | 17.985039
Scipy_Adaptive | 2.714020 | 0.978131

## Slide 21
UBFC Result For Scipy_Adaptive
20
MAE: 2.714020

## Slide 22
UBFC Result For Scipy_Adaptive
21
MAE: 18.082846

## Slide 23
Summary
Mean RGB
Extraction
CHROM/POS
Ground Truth
Line 0: [values of the BVP signal]
BVP Signal
Peak Detection
scipy_find_peaks
Aduptive
22
MAE
BPM
Peak-to-Peak Interval
BPM Calculation
Peak Detection Experiments
BVP Signal
pyVHR FrameWork
Find The Median For Each Block
Peak-to-Peak Interval
BPM Calculation
Find The Median For Each Block
Pure Dataset | MAE | Std Dev
Steady | 2.893107 | 1.760998
Talking | 4.918641 | 4.137012
Slow Translation | 3.372643 | 2.743749
Fast Translation | 2.332530 | 1.432035
Small Rotation | 3.113621 | 1.829347
Medium Rotation | 3.297898 | 1.666147
Full Dataset | 3.321407 | 2.261548
UBFC | MAE | Std Dev
Fulldataset | 2.714020 | 0.978131