## Slide 1
Rafsan Jany
Korean Convergence Medical Science
Deep Learning Experiments

## Slide 2
PyVHR WorkFlow
1
PyVHR does NOT provide any option for training deep learning models
out of the box.
It only provides inference using pre-trained models for its
deep-learning-based methods
MTTS-CAN
HR-CNN

## Slide 3
UBFC Result For MTTS_CAN
2
Average MAE (across all videos): 33.37
Standard Deviation of MAE: 18.13
Reference: https://github.com/phuselab/pyVHR/tree/master/results/h5

## Slide 4
UBFC Result For MTTS_CAN
3
Video_1
Video_29
Video_4
Video_12

## Slide 5
PURE Dataset For PyVHR
4
MTTS_CAN
Method | MAE | Std Dev
Steady | 3.13 | 3.72
Talking | 16.28 | 25.00
Slow Translation | 7.43 | 7.33
Fast Translation | 14.48 | 13.43
Small Rotation | 5.74 | 8.80
Medium Rotation | 11.54 | 14.08

## Slide 6
PURE Result For MTTS_CAN
5
Video_6
Steady | 
Talking | 
Slow Translation | 
Fast Translation | 
Small Rotation | 
Medium Rotation | 

## Slide 7
Fast Translation | 
Small Rotation | 
Medium Rotation | 
Steady | 
Talking | 
Slow Translation | 
PURE Result For MTTS_CAN
6
Video_8

## Slide 8
Input X
Output y
pyVHR Peak Detection Hybrid Experiment
Mean RGB
Extraction
Ground Truth
Line 0:
[values of
the
BVP signal]
BVP Signal
Peak Detection
scipy_find_peaks
Adaptive
7
MAE
BPM
Peak-to-Peak Interval
BPM Calculation
pyVHR FrameWork
Find The Median For Each Block
Peak Algo Frame
Neural Net Frame
Model Save
Model Load

## Slide 9
Workflow Overview
8
Step 1: Data Extraction (PyVHR)
pipe.run_on_video() takes a video and extracts:
filtered_windowed_sig → a list of RGB windows
Each window shape = (window_size, 3) → e.g., 240 x 3 if 8 seconds @ 30 FPS. Column 0 = Red signal over time Column 1 = Green signal Column 2 = Blue signal
Ground Truth BVP (bvp_gt) → segmented into gt_bvp_blocks for the
same time windows.
Step 2: Dataset (PURE) Class
The dataset does 3 main things:
Normalization → For each signal: (signal - mean) / std
Length Matching → Ground truth BVP is sampled at 60 Hz,
RGB at 30 Hz → downsample BVP to match RGB length.
Training Data – 47 Videos (Total Block – 2887)
Training Data – 12 Videos (Total Block – 689)
Dataset Contain Similar Number of:
Stedy,
Talking,
Slow Translation,
Fast Translation,
Small Rotation,
Medium Rotation)
rgb: tensor([[0.2, -0.1, 0.05], [0.3, -0.05, 0.06], ...]) # shape (240, 3)
bvp: tensor([-0.01, 0.02, 0.05, ...]) # shape (240,)
Step 3: DataLoader and Batch Size
DataLoader(train_dataset, batch_size=8, shuffle=True):
Groups 8 windows together in one batch.
rgb shape: (8, 240, 3) # 8 windows, each 240 samples long, 3 channels
bvp shape: (8, 240) # 8 corresponding BVP windows
Step 4: Model Input and Output
The CNN model expects:
Input: (batch_size, seq_len, 3) → (8, 240, 3)
It permutes to (batch_size, channels, seq_len) → (8, 3, 240) for Conv1D.
Inside CNN:
Conv layers slide over the time axis, learning temporal patterns in RGB.
Final output: (batch_size, 1, seq_len) → then squeeze → (batch_size, seq_len).
So prediction for each sample in batch = 240-length waveform.
Example: Input → (8, 240, 3) Output → (8, 240)
(Each row is a predicted BVP signal)

## Slide 10
Model Architecture
9
--------------------------------------------------------------
----------------------------------------------------------------
Layer (type) Output Shape Param #
================================================================
Conv1d-1 [-1, 32, 300] 512
ReLU-2 [-1, 32, 300] 0
Conv1d-3 [-1, 64, 300] 10,304
ReLU-4 [-1, 64, 300] 0
Conv1d-5 [-1, 64, 300] 20,544
ReLU-6 [-1, 64, 300] 0
Conv1d-7 [-1, 1, 300] 65
================================================================
Total params: 31,425
Trainable params: 31,425
Non-trainable params: 0
----------------------------------------------------------------
Input size (MB): 0.00
Forward/backward pass size (MB): 0.73
Params size (MB): 0.12
Estimated Total Size (MB): 0.86
----------------------------------------------------------------

## Slide 11
Result Anaslysis For 1D-CNN
10

## Slide 12
Experiment with Unet architecture
11
Improved U-Net Model to Estimate Cardiac Output Based on Photoplethysmography and Arterial Pressure Waveform [1]
Xichen Xu 1 , Qunfeng Tang 2,* and Zhencheng Chen 2,*
The authors state:
“In the study of non-invasive blood pressure estimation using PPG signals, U-Net performed very well, so we chose U-Net as the model architecture for this study.” (Page 6)
So, the main reasons for choosing U-Net are:
Its success in biomedical applications (especially for structured signal/image data).
It extracts and reconstructs features effectively.
[1] Xu, X.; Tang, Q.; Chen, Z. Improved U-Net Model to Estimate Cardiac Output Based on Photoplethysmography and Arterial Pressure Waveform.
Sensors 2023, 23, 9057. https://doi.org/10.3390/s23229057
The authors also state:
“U-Net is often used for two-dimensional images. In our study,
the input was a one-dimensional waveform signal,
and U-Net was modified to make it suitable for
one-dimensional signals.” (Page 6)
Modifications:
Replaced 2D convolutions with 1D convolutions.
Added bi-directional LSTM layers: -> One between encoder and decoder. -> One after the decoder, before the final output.
Added a fully connected (dense) layer at the end to output a scalar CO value.
Input: PPG + ART
Output:
Cardiac Output (CO) in L/min

## Slide 13
Their UNet VS Our UNet
12
3 16 16
16 32 32
32 64 64
16 32 32
3 16 16
32 64 64
32 64 64
U-Net Model + Bi LSTM
Mini U-Net Model
Layer/Block | Estimated Parameters
Encoder + Decoder (Conv1D, 4 levels) | 400K
Bi-LSTM (2 layers) | 500K per layer
Dense Layer | 50K
Total Estimate | 1.2 million
Estimated Size | 6/7 MB
Total params: 168,401
Trainable params: 168,401
----------------------------------------------------------------
Forward/backward pass size (MB): 1.02
Params size (MB): 0.64

## Slide 14
MINI UNet Summary
13
-------------------------- Layer--------------------------------
Layer (type) Output Shape Param #
=========================================
Conv1d-1 [-1, 16, 256] 160
ReLU-2 [-1, 16, 256] 0
Conv1d-3 [-1, 16, 256] 784
ReLU-4 [-1, 16, 256] 0
MaxPool1d-5 [-1, 16, 128] 0
Conv1d-6 [-1, 32, 128] 1,568
ReLU-7 [-1, 32, 128] 0
Conv1d-8 [-1, 32, 128] 3,104
ReLU-9 [-1, 32, 128] 0
MaxPool1d-10 [-1, 32, 64] 0
Conv1d-11 [-1, 64, 64] 6,208
ReLU-12 [-1, 64, 64] 0
Conv1d-13 [-1, 64, 64] 12,352
ReLU-14 [-1, 64, 64] 0
MaxPool1d-15 [-1, 64, 32] 0
Conv1d-16 [-1, 128, 32] 24,704
ReLU-17 [-1, 128, 32] 0
Conv1d-18 [-1, 128, 32] 49,280
ReLU-19 [-1, 128, 32] 0
ConvTranspose1d-20 [-1, 64, 64] 16,448
Conv1d-21 [-1, 64, 64] 24,640
ReLU-22 [-1, 64, 64] 0
Conv1d-23 [-1, 64, 64] 12,352
ReLU-24 [-1, 64, 64] 0
ConvTranspose1d-25 [-1, 32, 128] 4,128
Conv1d-26 [-1, 32, 128] 6,176
ReLU-27 [-1, 32, 128] 0
Conv1d-28 [-1, 32, 128] 3,104
ReLU-29 [-1, 32, 128] 0
ConvTranspose1d-30 [-1, 16, 256] 1,040
Conv1d-31 [-1, 16, 256] 1,552
ReLU-32 [-1, 16, 256] 0
Conv1d-33 [-1, 16, 256] 784
ReLU-34 [-1, 16, 256] 0
Conv1d-35 [-1, 1, 256] 17
----------------------------------------------------------------
Encoder 1
3 -> 16-> 16
Encoder 2
16 -> 32 -> 32
Encoder 3
32 -> 64 -> 64
Output
Bottlneck
32 -> 64 -> 64
Decoder 1
3 -> 16-> 16
Decoder 2
16 -> 32 -> 32
Decoder 3
32 -> 64 -> 64
Input

## Slide 15
MINI UNet Summary
14
Encoder 1
Sequential(
(0): Conv1d(3, 16, kernel_size=(3,), stride=(1,), padding=(1,))
(1): ReLU()
(2): Conv1d(16, 16, kernel_size=(3,), stride=(1,), padding=(1,))
(3): ReLU()
)
Encoder 2
Sequential(
(0): Conv1d(16, 32, kernel_size=(3,), stride=(1,), padding=(1,))
(1): ReLU()
(2): Conv1d(32, 32, kernel_size=(3,), stride=(1,), padding=(1,))
(3): ReLU()
)
Encoder 3
Sequential(
(0): Conv1d(32, 64, kernel_size=(3,), stride=(1,), padding=(1,))
(1): ReLU()
(2): Conv1d(64, 64, kernel_size=(3,), stride=(1,), padding=(1,))
(3): ReLU()
)
Sequential(
(0): Conv1d(64, 128, kernel_size=(3,), stride=(1,), padding=(1,)) || (1): ReLU(),
(2): Conv1d(128, 128, kernel_size=(3,), stride=(1,), padding=(1,))
(3): ReLU()
)
(Batch, Channels, Sequence Length) = (8, 3, 240)
(pool1): MaxPool1d(kernel_size=2, stride=2, padding=0, dilation=1,
ceil_mode=False)
(pool2): MaxPool1d(kernel_size=2, stride=2, padding=0, dilation=1, ceil_mode=False)
(pool3): MaxPool1d(kernel_size=2, stride=2, padding=0, dilation=1, ceil_mode=False)
(final_conv): Conv1d(16, 1, kernel_size=(1,), stride=(1,))
Decoder 1
Sequential(
(0): Conv1d(32, 16, kernel_size=(3,), stride=(1,), padding=(1,))
(1): ReLU()
(2): Conv1d(16, 16, kernel_size=(3,), stride=(1,), padding=(1,))
(3): ReLU()
)
Decoder 2
Sequential(
(0): Conv1d(64, 32, kernel_size=(3,), stride=(1,), padding=(1,))
(1): ReLU()
(2): Conv1d(32, 32, kernel_size=(3,), stride=(1,), padding=(1,))
(3): ReLU()
)
Decoder 3
Sequential(
(0): Conv1d(128, 64, kernel_size=(3,), stride=(1,), padding=(1,))
(1): ReLU()
(2): Conv1d(64, 64, kernel_size=(3,), stride=(1,), padding=(1,))
(3): ReLU()
)
(up1): ConvTranspose1d(32, 16, kernel_size=(2,), stride=(2,))
(up2): ConvTranspose1d(64, 32, kernel_size=(2,), stride=(2,))
(up3): ConvTranspose1d(128, 64, kernel_size=(2,), stride=(2,))
torch.cat((d1, e1), dim=1)
torch.cat((d2, e2), dim=1)
torch.cat((d3, e3), dim=1)
Total params: 168,401 or 0.168 million
Trainable params: 168,401 or 0.168 million
Forward/backward pass size (MB): 1.02
Params size (MB): 0.64
Estimated Total Size (MB): 1.66

## Slide 16
How Realy Unet Works
15
Encoder Path (Downsampling)
The encoder applies Conv + ReLU + Pooling in stages.
What it does:
Extracts hierarchical features from the input signal.
Each layer captures patterns at different time scales:
  Early layers: Fine details (small peaks, local oscillations).
  Deeper layers: Coarse features (overall HR trend, global waveform shape).
  Detect edges, peaks, frequency patterns.
Bottleneck
What it does:
  Acts as a global feature extractor. (small peaks, local oscillations).
  Knows "what the signal looks like overall" — frequency pattern, noise characteristics.
Decoder Path (Upsampling)
What it does:
Upsamples back to original resolution using ConvTranspose (or interpolation).
Reconstruct a signal with original length and shape.
It lets the model use both the overall signal context
The decoder gets direct access to early high-resolution features.

## Slide 17
Result Basic FOR MINI UNet For PURE
16

## Slide 18
MAE Loss Definition:
Ensures the overall waveform shape is close to GT.
MAE looks at the difference in the time domain:
Problem with only MAE (or MSE):
If predicted waveform is smooth but lacks the correct periodic structure, MAE
might still be low.
This happens because point-wise error does not care about frequency components.
MAE Loss
17
[1] S. Pascual, A. Bonafonte, and J. Serrà, "SEGAN: Speech Enhancement Generative Adversarial Network," arXiv preprint arXiv:1703.09452, 2017.
[2]C. Little, D. Mclean, K. Crockett and B. Edmonds, "A Semantic and Syntactic Similarity Measure for Political Tweets," in IEEE Access, vol. 8, pp.
154095-154113, 2020, doi: 10.1109/ACCESS.2020.3017797
[3] J. M. Donahue, B. Li, and A. Misra, "Wave-U-Net: A multi-scale neural network for end-to-end audio source separation,"
Available: https://arxiv.org/abs/1806.03185

## Slide 19
FFT LOSS
18
[1] S. Pascual, A. Bonafonte, and J. Serrà, "SEGAN: Speech Enhancement Generative Adversarial Network," arXiv preprint arXiv:1703.09452, 2017.
[2]C. Little, D. Mclean, K. Crockett and B. Edmonds, "A Semantic and Syntactic Similarity Measure for Political Tweets," in IEEE Access, vol. 8, pp.
154095-154113, 2020, doi: 10.1109/ACCESS.2020.3017797
[3] J. M. Donahue, B. Li, and A. Misra, "Wave-U-Net: A multi-scale neural network for end-to-end audio source separation,"
Available: https://arxiv.org/abs/1806.03185
FFT Loss Definition
Compute Fast Fourier Transform (FFT) for
both predicted and ground truth signals.
Compare their magnitude spectra
instead of time-domain values:
Intuition:
If both signals have the same frequency content, their periodic structure (heart-rate bands) matches.
Forces the model to learn frequency characteristics, not just point-by-point amplitude.
Why FFT Loss Helps
Signals like BVP, ECG, speech are dominated
by specific frequency bands.
Matching frequency domain ensures:
✔ HR-related components are preserved.
✔ No over-smoothed predictions.
Combined with MAE:
→ Gives time-domain accuracy + frequency-domain fidelity.

## Slide 20
FFT LOSS + MAE LOSS
19
[1] S. Pascual, A. Bonafonte, and J. Serrà, "SEGAN: Speech Enhancement Generative Adversarial Network," arXiv preprint arXiv:1703.09452, 2017.
[2]C. Little, D. Mclean, K. Crockett and B. Edmonds, "A Semantic and Syntactic Similarity Measure for Political Tweets," in IEEE Access, vol. 8, pp.
154095-154113, 2020, doi: 10.1109/ACCESS.2020.3017797
[3] J. M. Donahue, B. Li, and A. Misra, "Wave-U-Net: A multi-scale neural network for end-to-end audio source separation,"
Available: https://arxiv.org/abs/1806.03185
MAE (Time Domain)
Ensures the overall waveform shape is close to GT.
Without it, the signal could have correct frequency but wrong amplitude or offset.
FFT Loss (Frequency Domain)
Ensures the periodicity (rhythm) and frequency components (heart-rate bands) match GT.
Without it, the signal might look smooth but miss the actual rhythm.

## Slide 21
Input X
Output y
pyVHR Peak Detection Unet[fft loss] Experiment
Mean RGB
Extraction
Ground Truth
Line 0:
[values of
the
BVP signal]
BVP Signal
Peak Detection
scipy_find_peaks
Adaptive
20
MAE
BPM
Peak-to-Peak Interval
BPM Calculation
pyVHR FrameWork
Find The Median For Each Block
Peak Algo Frame
Neural Net Frame
Encoder 1
3 -> 16-> 16
Encoder 2
16 -> 32 -> 32
Encoder 3
32 -> 64 -> 64
Bottlneck
32 -> 64 -> 64
Decoder 1
3 -> 16-> 16
Decoder 2
16 -> 32 -> 32
Decoder 3
32 -> 64 -> 64
FFt Loss + MAE Loss
Optimization
Forward Pass
Back Propagation
Model Load
Model Load

## Slide 22
Result Basic FOR MINI UNet For PURE
21

## Slide 23
BPM + Peak -> Test Data
22
Method | MAE | Std Dev
Median | 0.824 | 0.312
Mean | 1.908 | 0.818

## Slide 24
BPM + Peak -> Train Data
23
Method | MAE | Std Dev
Median | 1.148 | 0.859
Mean | 1.996 | 1.932

## Slide 25
Result Basic FOR MINI UNet For PURE
24
Evaluating Test Subject: 09.avi
Steady
Talking
Slow
Translation

## Slide 26
Result Basic FOR MINI UNet For PURE
25
Evaluating Test Subject: 09.avi
Fast
Translation
Small
Rotation
Medium
Rotation

## Slide 27
Peaks
26
Ground Truth BVP
Generated BVP

## Slide 28
Peaks Worst Case
27
Ground Truth BVP
Generated BVP
MAE : 5.077
MAE : 5.81
MAE : 5.0044

## Slide 29
Result For UBFC Dataset [Trained on only Train Data From PURE]
28
Method | MAE | Std Dev
Median | 2.43 | 1.34
Mean | 2.94 | 1.42

## Slide 30
Peaks
29
Ground Truth BVP
Generated BVP

## Slide 31
Peaks Worst Case
30
Ground Truth BVP
Generated BVP
MAE: 50.7692
MAE: 43.2692
MAE: 45.8333