## Slide 1
Rafsan Jany
Korean Convergence Medical Science
Paper Review and Phase Alignment

## Slide 2
1
Study - 1
Paper Name: Performance Evaluation of rPPG Approaches with and without the Region-of-Interest Localization Step (Žan Pirnar, Miha Finžgar, Primož Podržaj, 2021)
Description:
The study investigates whether ROI localization is essential for remote photoplethysmography (rPPG). Traditionally, ROI detection (like face or skin segmentation) is considered necessary before extracting signals, but newer
approaches (like Full Video Pulse Extraction, FVP) skip this step. The paper evaluates both strategies.
Methods:
ROI-based approaches tested: (a) VK (Viola-Jones face detector + ROI cropping + KLT tracker) (b) VK-LMK (Viola-Jones + facial landmarks + KLT)
(c) VK-Conaire (Viola-Jones + mutual information-based skin detector + KLT) (d) VK-RGBHCbCr (Viola-Jones + skin-color segmentation + KLT)
Without ROI: FVP (Full Video Pulse Extraction)
NOTE
Viola–Jones face detector → Classic fast algorithm for detecting faces in images. (2001)
KLT (Kanade–Lucas–Tomasi) → Tracker that follows feature points across video frames. (1981 / 1991)
Mutual information–based skin detector → Segments skin regions by maximizing statistical similarity between skin models and image data. (2007)
FVP (Full Video Pulse Extraction) → Uses the whole video (no ROI) to extract average color signals for rPPG. (2018)

## Slide 3
2
Study - 1
Paper Name: Performance Evaluation of rPPG Approaches with and without the Region-of-Interest Localization Step (Žan Pirnar, Miha Finžgar, Primož Podržaj, 2021)
Algorithms for rPPG extraction:
POS (Plane-Orthogonal-to-Skin) → model-based, robust to noisy ROIs
2SR (Spatial Subspace Rotation) → data-driven, more sensitive to noise
Datasets used:
PURE (controlled lab scenarios, head motion/talking)
LGI-PPGI-FVD (real-world, including gym exercise)
PBDTrPPG (challenging lighting, skin tone variations, lossy compression)
ROI sizes (in pixels) expressed as a mean ± standard deviation for different image-processing front-ends and all studied data sets:
Dataset | VK | VK-LMK | VK-RGBHCbCr | VK-Conaire
PURE | 19,063 ± 3,581 | 9,114 ± 1,591 | 13,407 ± 5,339 | 19,984 ± 5,252
PBDTrPPG | 28,849 ± 14,196 | 12,731 ± 4,498 | 19,514 ± 16,015 | 19,128 ± 9,699
LGI-PPGI-FVD | 38,060 ± 13,863 | 14,962 ± 7,106 | 32,916 ± 12,141 | 40,550 ± 15,970
The numbers are the average pixel area of the detected ROI per dataset and method, with ± showing variability across recordings.
Example: PURE – VK = 19,063 ± 3,581 On average, the face ROI covers ~19,000 pixels in those videos, with a variation of ±3,581 pixels depending on subject and frame.
How 2SR works (2014, 2016)
Take all skin pixels (from ROI or full frame).
Represent them as a cloud of points in RGB space.
Over time, this point cloud rotates slightly due to periodic blood volume changes (color modulation from pulse).
2SR tracks this rotation to estimate pulse-related signals.

## Slide 4
3
Study - 1
Paper Name: Performance Evaluation of rPPG Approaches with and without the Region-of-Interest Localization Step (Žan Pirnar, Miha Finžgar, Primož Podržaj, 2021)
Metrics:
Success rate (how often methods worked) FVP (no ROI) → 100% success. ROI-based methods: VK-RGBHCbCr → 88.37% VK-Conaire → 94.19% VK and VK-LMK → 95.35% Reason for failures: Face not detected in first frame (Viola–Jones fail) KLT tracker lost all feature points Skin segmentation failed (no skin pixels detected)
SNR of extracted signals General finding: SNR differences between methods were not statistically significant in many scenarios (especially resting, talking , skin tone). POS algorithm consistently gave higher SNR than 2SR. FVP sometimes had lower SNR (under motion, low light). Trends observed: Higher light → higher SNR Darker skin → lower SNR Motion (talking, rotation) → lower SNR
RMSE between reference PR (pulse rate) and estimated PR : [NXT PAGE]

## Slide 5
4
Study - 1
SB->POS
Dataset / Scenario | VK (SB) | VK (2SR) | VK-LMK (SB) | VK-LMK (2SR) | VK-RGBHCbCr (SB) | VK-RGBHCbCr (2SR) | VK-Conaire (SB) | VK-Conaire (2SR) | FVP (SB)
PURE – resting | 1.08 ± 0.71 (10) | 1.11 ± 0.72 (10) | 1.09 ± 0.74 (10) | 1.18 ± 0.72 (10) | 1.31 ± 0.91 (9) | 1.50 ± 1.29 (9) | 1.09 ± 0.75 (10) | 1.13 ± 0.78 (10) | 1.48 ± 0.86 (10)
PURE – talking | 4.09 ± 3.68 (9) | 8.19 ± 15.62 (9) | 11.08 ± 15.72 (9) | 14.54 ± 20.24 (9) | 8.68 ± 16.24 (8) | 9.06 ± 17.59 (8) | 8.48 ± 9.50 (9) | 12.7 ± 16.58 (9) | 7.95 ± 9.32 (9)
PURE – head trans. | 1.07 ± 0.64 (20) | 1.14 ± 0.75 (20) | 1.13 ± 0.83 (20) | 1.20 ± 0.87 (20) | 1.13 ± 0.74 (18) | 1.28 ± 0.80 (18) | 1.14 ± 0.71 (20) | 2.98 ± 4.18 (20) | 3.96 ± 4.97 (20)
PURE – head rot. | 0.88 ± 0.70 (20) | 0.84 ± 0.62 (20) | 1.06 ± 0.97 (20) | 5.53 ± 6.62 (20) | 0.84 ± 0.62 (20) | 5.41 ± 12.43 (20) | 3.08 ± 6.29 (20) | 9.45 ± 17.76 (20) | 2.47 ± 5.73 (20)
PBDTrPPG – LC1 | 25.57 ± 12.25 (3) | 25.23 ± 13.09 (3) | 23.27 ± 12.02 (3) | 22.92 ± 11.40 (3) | 19.66 ± 11.69 (2) | 19.85 ± 12.71 (2) | 24.56 ± 12.37 (3) | 23.89 ± 12.15 (3) | 52.28 ± 6.65 (3)
PBDTrPPG – LC2 | 22.69 ± 13.27 (3) | 25.78 ± 16.04 (3) | 21.47 ± 13.42 (3) | 23.81 ± 16.56 (3) | 20.47 ± 12.70 (3) | 21.55 ± 12.59 (3) | 18.95 ± 11.40 (3) | 24.79 ± 16.89 (3) | 54.84 ± 9.41 (3)
PBDTrPPG – LC3 | 17.37 ± 10.36 (3) | 30.53 ± 28.34 (3) | 21.88 ± 22.58 (3) | 27.15 ± 28.57 (3) | 20.23 ± 12.79 (3) | 22.39 ± 15.64 (3) | 18.03 ± 11.19 (3) | 23.26 ± 17.84 (3) | 52.17 ± 17.90 (3)
PBDTrPPG – LC4 | 12.84 ± 9.61 (3) | 17.36 ± 15.22 (3) | 15.12 ± 13.10 (3) | 16.65 ± 15.11 (3) | 14.36 ± 10.67 (3) | 13.03 ± 8.97 (3) | 14.44 ± 9.65 (3) | 17.82 ± 13.57 (3) | 40.76 ± 26.12 (3)
PBDTrPPG – LC5 | 12.44 ± 9.62 (3) | 20.96 ± 19.39 (3) | 15.81 ± 16.58 (3) | 19.43 ± 22.08 (3) | 19.76 ± 14.65 (3) | 17.20 ± 15.28 (3) | 24.94 ± 15.35 (3) | 27.90 ± 17.85 (3) | 40.62 ± 29.02 (3)
PBDTrPPG – bright | 4.37 ± 1.98 (5) | 4.16 ± 1.46 (5) | 4.14 ± 1.63 (5) | 4.28 ± 1.60 (5) | 4.27 ± 1.88 (5) | 4.24 ± 1.53 (5) | 4.10 ± 1.55 (5) | 4.08 ± 1.47 (5) | 32.02 ± 22.30 (5)
PBDTrPPG – interm. | 21.13 ± 10.92 (5) | 21.64 ± 10.51 (5) | 16.59 ± 11.79 (5) | 16.11 ± 10.76 (5) | 21.41 ± 7.05 (5) | 20.47 ± 9.00 (5) | 25.30 ± 8.61 (5) | 26.17 ± 8.79 (5) | 43.74 ± 3.15 (5)
PBDTrPPG – dark | 29.05 ± 3.53 (5) | 46.12 ± 12.79 (5) | 37.80 ± 9.02 (5) | 45.59 ± 13.34 (5) | 33.85 ± 3.51 (4) | 34.66 ± 6.08 (4) | 31.14 ± 3.05 (5) | 40.35 ± 6.07 (5) | 68.65 ± 9.62 (5)
LGI-PPGI – resting | 2.22 ± 1.30 (6) | 2.20 ± 1.31 (6) | 2.23 ± 1.30 (6) | 2.21 ± 1.31 (6) | 2.08 ± 1.38 (6) | 2.18 ± 1.32 (6) | 2.20 ± 1.31 (6) | 2.20 ± 1.32 (6) | 2.24 ± 1.31 (6)
LGI-PPGI – gym | 13.9 ± 11.16 (2) | 15.6 ± 12.89 (2) | 17.81 ± 9.53 (2) | 33.5 ± 4.35 (2) | 2.99 ± 0.0 (1) | 31.84 ± 0.0 (1) | 13.77 ± 0.0 (1) | 29.6 ± 0.0 (1) | 39.66 ± 17.22 (6)

## Slide 6
5
Study - 1
Paper Name: Performance Evaluation of rPPG Approaches with and without the Region-of-Interest Localization Step (Žan Pirnar, Miha Finžgar, Primož Podržaj, 2021)
Strengths
Comprehensive comparison across different ROI strategies and no-ROI approach.
Used multiple datasets (controlled + real-world + compression effects).
Evaluated with both model-based (POS) and data-driven (2SR) rPPG algorithms.
Clearly reported limitations (failures of detectors, challenges with compression/skin tone).
Weaknesses
Did not analyze computational complexity, which is important for real-time systems.
Limited number of video recordings in motion/skin tone tests.
ROI quality not directly quantified (skin vs non-skin pixel ratio not deeply studied).
Only focused on face-based signals, not other body regions.
Conclusions
ROI localization is not strictly necessary: FVP performed reliably, though sometimes less accurate.
Algorithm choice matters more than ROI choice: POS outperformed 2SR in robustness.
For real-world deployment, ROI localization might improve accuracy, but FVP offers robustness when ROI detection fails.

## Slide 7
6
Study - 2
Paper Name: Assessment of ROI Selection for Facial Video-Based rPPG Authors: Dae-Yeol Kim, Kwangkee Lee & Chae-Bong Sohn (2021)
Description:
To investigate how different facial Regions of Interest (ROIs) affect the accuracy of rPPG algorithms by considering skin thickness and anatomical features.
Methods
Datasets UBFC-rPPG (42 subjects, 10 s videos). LGI-PPGI (6 subjects, motion/no-motion/dialog/gym)
Algorithms tested (7 total): CHROM, GREEN, ICA, PBV, POS, SSR, LGI
ROI candidates: Anatomical mapping of 39 regions Reduced to 31 ROIs for experiments
Metrics: MAE, RMSE, PCC → combined into rBS (relative BVP similarity).
Tools: Face mesh via MediaPipe (468 landmarks).

## Slide 8
7
Study - 2
Paper Name:Assessment of ROI Selection for Facial Video-Based rPPG Authors: Dae-Yeol Kim, Kwangkee Lee & Chae-Bong Sohn (2021)
Key Results
ROIs with thin skin and large surface area yielded better signals.
Best ROIs (TOP-5): Right malar (27), Glabella (10), Lower medial forehead (3), Upper medial forehead (0), Left malar (28).
Worst ROIs (BOT-5): Left lower nasal sidewall (15), Right mid nasal sidewall (12), Left mid nasal sidewall (13), Lower cheek (20), Right upper lip (19).
Performance vs. ROI
TOP-5 regions consistently outperformed whole-face ROI and BOT-5 across both datasets.
UBFC dataset (POS method): MAE: 1.85 (TOP-5) vs. 1.87 (whole face) vs. 7.26 (BOT-5). PCC: 0.80–0.87 (TOP-5/whole face) vs. 0.29–0.36 (BOT-5).
LGI dataset: MAE: 2.93–3.61 (TOP-5) vs. 4.04 (whole face) vs. 6.21–10.71 (BOT-5).
Dataset | Metric | POS (TOP-5) | POS (Face+Skin) | POS (BOT-5) | CHROM (TOP-5) | CHROM (Face+Skin) | CHROM (BOT-5)
UBFC | MAE | 1.85 | 1.87 | 7.26 | 1.50 | 2.67 | 5.90
 | PCC | 0.80 | 0.85 | 0.29 | 0.87 | 0.80 | 0.36
LGI | MAE | 3.61 | 4.04 | 6.21 | 2.93 | 4.04 | 10.71
 | PCC | 0.34 | 0.30 | 0.30 | 0.59 | 0.38 | 0.35

## Slide 9
8
Study - 2
Paper Name:Assessment of ROI Selection for Facial Video-Based rPPG Authors: Dae-Yeol Kim, Kwangkee Lee & Chae-Bong Sohn (2021)
Core Takeaway
Cheeks (malar) + forehead (medial/lower) + glabella are the most reliable ROIs for rPPG.
Nasal/upper lip regions perform worst due to thicker skin and higher noise.
Skin thickness is a key anatomical determinant of rPPG signal quality.

## Slide 10
9
Study - 3
Paper Name: Optimal signal quality index for remote photoplethysmogram sensingAuthors: Mohamed Elgendi, Igor Martinelli & Carlo Menon (2024)
Description:
To identify the most effective Signal Quality Index (SQI) for rPPG signals and propose a single practical SQI threshold that can be implemented on portable/mobile devices for real-time quality assessment.
Methods
Datasets used: PURE dataset (10 subjects, 60 sequences, head movements).
LGI-PPGI dataset (6 subjects, 24 videos, resting/gym/talk/rotation).
rPPG algorithms tested (via pyVHR):CHROM, GREEN, OMIT, POS, LGI, PBV, ICA, PCAs.
Facial regions: 44 landmarks across forehead + left cheek + right cheek, extracted with MediaPipe Face Meshs.
Window sizes tested: 1–12 seconds. SQIs tested (8 total): NSQI, KSQI, PSQI, SSQI, ESQI, MSQI, ZSQI, RSQIs.
Classification: Signals labeled into Excellent / Acceptable / Unfit (based on ΔBPM ≤5, DTW, and correlation r).
Classifiers used: SVM, LDA, Logistic Regression, Decision Tree.

## Slide 11
10
Study - 3
Paper Name: Optimal signal quality index for remote photoplethysmogram sensing
Authors: Mohamed Elgendi, Igor Martinelli & Carlo Menon (2024)
Signal Quality Indices (SQIs)
NSQI (Normalized SQI) → Measures energy of HR frequency vs. noise; normalizes spectrum to highlight pulse peaks. Compares energy in HR-related band to total signal energy.
where 𝑃Hrband is spectral power near HR frequency (±Δ), and 𝑃total is total spectral power.
KSQI (Kurtosis-based SQI) → Looks at “peakedness” of the waveform; clean periodic signals show sharper peaks. Measures how “peaked” the signal distribution is (clean signals have high kurtosis).
          where 𝜇4 = 4th central moment, 𝜎 = standard deviation.
PSQI (Power Spectrum SQI) → Compares power at HR frequency vs. rest of spectrum; strong HR → higher PSQI. Checks if the HR frequency peak dominates the spectrum.
where 𝑃(𝑓) is the power spectrum.

## Slide 12
11
Study - 3
Paper Name: Optimal signal quality index for remote photoplethysmogram sensing
Authors: Mohamed Elgendi, Igor Martinelli & Carlo Menon (2024)
Signal Quality Indices (SQIs)
SSQI (Skewness-based SQI) → Evaluates asymmetry of the signal distribution; motion/noise makes it more skewed. Measures asymmetry of the signal distribution.
where 𝜇3 = 3rd central moment, 𝜎 = standard deviation.
ESQI (Entropy-based SQI) → Measures randomness/complexity; lower entropy = cleaner signal. Measures randomness; low entropy means structured/periodic signal (better).
where 𝑝(𝑥) is the probability distribution of signal amplitudes.
MSQI (Mean-based SQI) → Uses average signal stability; unstable means poor quality. Uses stability of the mean to check quality. Compute moving average of the signal. MSQI = variance of that moving mean (lower = cleaner).

## Slide 13
12
Study - 3
Paper Name: Optimal signal quality index for remote photoplethysmogram sensing
Authors: Mohamed Elgendi, Igor Martinelli & Carlo Menon (2024)
Signal Quality Indices (SQIs)
ZSQI (Zero-crossing SQI) → Counts how often the signal crosses zero; regular crossings = rhythmic pulse. Counts regularity of zero-crossings. Clean periodic signals → regular crossings.
RSQI (Relative power SQI) → Ratio of HR frequency band power to total power; higher ratio = better HR content. Fraction of spectral energy within HR range.

## Slide 14
13
Study - 3
Paper Name: Optimal signal quality index for remote photoplethysmogram sensing
Authors: Mohamed Elgendi, Igor Martinelli & Carlo Menon (2024)
Signal Quality Indices (SQIs)
ZSQI (Zero-crossing SQI) → Counts how often the signal crosses zero; regular crossings = rhythmic pulse. Counts regularity of zero-crossings. Clean periodic signals → regular crossings.
RSQI (Relative power SQI) → Ratio of HR frequency band power to total power; higher ratio = better HR content. Fraction of spectral energy within HR range.

## Slide 15
14
Study - 3
Paper Name: Optimal signal quality index for remote photoplethysmogram sensing
Authors: Mohamed Elgendi, Igor Martinelli & Carlo Menon (2024)
Distribution of reconstructed signals by rPPG methods across different window sizes
Excellent 75
Acceptable 35
Unfit 362
Excellent 125
Acceptable 74
Unfit 273
Excellent 143
Acceptable 85
Unfit 245

## Slide 16
15
Study - 3
Paper Name: Optimal signal quality index for remote photoplethysmogram sensing
Authors: Mohamed Elgendi, Igor Martinelli & Carlo Menon (2024)
SQI Performance
PURE dataset NSQI best for Excellent vs Unfit (OF1 = 0.86). KSQI best for Acceptable vs Unfit (OF1 = 0.81).
LGI-PPGI dataset NSQI best for Excellent vs Unfit (OF1 = 0.77). KSQI again best for Acceptable vs Unfit (OF1 = 0.68).
Threshold Proposed NSQI < 0.293 as the practical threshold for selecting high-quality frames

## Slide 17
16
Study - 4
Paper Name: The role of face regions in remote photoplethysmography for contactless heart rate monitoring
Authors: Maksym Bondarenko, Carlo Menon & Mohamed Elgendi (2025)
Description:
To systematically review 70 studies and analyze how the choice and number of Regions of Interest (ROIs: hole face, forehead, cheeks, nose, chin, multiple patches) influence the accuracy of rPPG-based heart rate (HR) estimation.
Methods:
Excluded: non-RGB, NIR/IR, theoretical, non-facial or contact-based methods.
Datasets analyzed: 20 public sets (UBFC-rPPG, PURE, COHFACE, VIPL-HR, MAHNOB-HCI).
Metrics: MAE (Mean Absolute Error) and RMSE (Root Mean Square Error).
ROI Selection
Most common: holistic (whole) face (36.8% of studies).
Best performing: forehead (24.5%) and cheeks (21.7%), due to large flat skin surfaces, stable perfusion, low hair/accessory interference .
Nose and chin were less reliable (6.6% and 4.7%).
ROI Quantity
More ROIs generally improved performance, but diminishing returns beyond ~60 patches.
Best results clustered around 3 ROIs and ~60 ROIs (LOESS analysis, Fig. 4).
Too many patches (>100) increased computation and sometimes added noise.

## Slide 18
17
Study - 4
Paper Name: The role of face regions in remote photoplethysmography for contactless heart rate monitoring
Authors: Maksym Bondarenko, Carlo Menon & Mohamed Elgendi (2025)
ROI Selection
Most common: holistic (whole) face (36.8% of studies).
Best performing: forehead (24.5%) and cheeks (21.7%), due to large flat skin surfaces, stable perfusion, low hair/accessory interference .
Nose and chin were less reliable (6.6% and 4.7%).

## Slide 19
18
Study - 4
Paper Name: The role of face regions in remote photoplethysmography for contactless heart rate monitoring
Authors: Maksym Bondarenko, Carlo Menon & Mohamed Elgendi (2025)
ROI Quantity
More ROIs generally improved performance, but diminishing returns beyond ~60 patches.
Best results clustered around 3 ROIs and ~60 ROIs.
Too many patches (>100) increased computation and sometimes added noise.

## Slide 20
19
Study - 4
Paper Name: The role of face regions in remote photoplethysmography for contactless heart rate monitoring
Authors: Maksym Bondarenko, Carlo Menon & Mohamed Elgendi (2025)
Performance Results
Algorithm / Model | UBFC MAE / RMSE | PURE MAE / RMSE | COHFACE MAE / RMSE | VIPL-HR MAE / RMSE | MAHNOB-HCI MAE / RMSE
MAR-rPPG (Qian et al. 2024) | 0.17 / 0.41 | 0.37 / 0.68 | – | 4.36 / 6.92 | –
TokenLearner rPPG (Zhao et al. 2024) | 0.12 / 0.35 | 0.08 / 0.29 | – | – | –
Dual-GAN rPPG (Hao Lu et al. 2021) | 0.44 / 0.67 | 0.82 / 1.31 | – | 4.93 / 7.68 | –
Graph-based rPPGNet (Si-Qi Liu et al. 2024) | 0.31 / 0.98 | 0.18 / 0.41 | 0.64 / 1.89 | 3.13 / 3.97 | –
Traditional ROI + ML Fusion (Yaran Duan et al. 2023) | 2.78 / 3.35 | 2.76 / 4.15 | 2.77 / 3.87 | 3.45 / 4.17 | –

## Slide 21
20
Study - 4
Paper Name: The role of face regions in remote photoplethysmography for contactless heart rate monitoring
Authors: Maksym Bondarenko, Carlo Menon & Mohamed Elgendi (2025)
Core Takeaway
ROI choice matters: cheeks + forehead consistently outperform nose/chin; whole face is common but not optimal.
Multiple ROIs help, but >60 adds little benefit and increases cost.
ML-based ROI fusion methods achieve MAE <0.5 bpm on best datasets, making rPPG competitive with contact PPG in controlled conditions.

## Slide 22
21
Study - 5
Paper Name: A comprehensive review of heart rate measurement using remote photoplethysmography and deep learning
Authors: Uday Debnath & Sungho Kim (2025)
Description:
The study systematically reviews 145 papers (2008–early 2025) on rPPG-based heart rate measurement with a focus on deep learning approaches. The goal is to compare conventional vs. deep learning methods, highlight datasets, performance, limitations, and outline future research directions.
Methods:
Followed PRISMA guidelines for systematic review.
Search terms: rPPG, heart rate, deep learning, RGB camera, non-contact monitoring.
Databases: Scopus, IEEE Xplore, Elsevier, Springer, Google Scholar.
Inclusion: peer-reviewed, English, full-text, 2008–2025, RGB camera based.
Exclusion: medical-only, infrared/radar/thermal sensors.
Result: 145 relevant articles.
Datasets in rPPG
Commonly used: MAHNOB-HCI, PURE, VIPL-HR, COHFACE, UBFC-rPPG, NBHR (newborn), TokyoTech, MMSE-HR, MMPD.
Ground truth usually from Pulse Oximeter; some use ECG.
Newer datasets (MMPD) include diverse skin tones, multiple lighting conditions, and motion scenarios .

## Slide 23
22
Study - 5
Paper Name: A comprehensive review of heart rate measurement using remote photoplethysmography and deep learning
Authors: Uday Debnath & Sungho Kim (2025)
Conventional rPPG Approaches
Signal extraction & processing:ICA, PCA, JADE, FastICA → BSS to isolate HR signals.
CHROM → color-difference model to reduce motion noise.
GREEN channel → hemoglobin absorption peak (520–580 nm).
POS (Plane-Orthogonal-to-Skin) → skin tone normalization.
SSR/2SR (Spatial Subspace Rotation) → rotation of color subspace.
Deep Learning Approaches
CNN-based models: DeepPhys, DeeprPPG, ResNet, MTTS-CAN.
GAN-based: PulseGAN (denoising HR waveform).
Attention models: ETA-rPPGNet, Spatial–Temporal Attention Nets.
Hybrid approaches: Combine BSS with CNNs or GANs.
Advantages: handle motion, low light, skin tone variation better.
Results: Deep models consistently outperform traditional ones in RMSE/MAE across datasets .
Datasets in rPPG
Commonly used: MAHNOB-HCI, PURE, VIPL-HR, COHFACE, UBFC-rPPG, NBHR (newborn), TokyoTech, MMSE-HR, MMPD.
Ground truth usually from Pulse Oximeter; some use ECG.
Newer datasets (MMPD) include diverse skin tones, multiple lighting conditions, and motion scenarios .

## Slide 24
23
Study - 5
Result
Proposed Method | Dataset(s) | Metrics Reported | Results
DeeprPPG | UBFC-rPPG | MAE, RMSE, r | MAE=1.36, RMSE=2.56, r=0.98
ETA-rPPGNet | UBFC-rPPG | MAE, RMSE, r | MAE=0.89, RMSE=1.56, r=0.99
MTTS-CAN | VIPL-HR, PURE | MAE, RMSE | MAE=1.07, RMSE=2.25
PhysNet | PURE | MAE, RMSE | MAE=2.04, RMSE=3.91
DeepPhys | PURE | MAE, RMSE | MAE=2.51, RMSE=4.12
HR-CNN | UBFC-rPPG | MAE, r | MAE=1.72, r=0.97

## Slide 25
24
Study - 5
Result
Proposed Method | Dataset(s) | Metrics Reported | Results
PulseGAN | VIPL-HR, PURE | MAE, RMSE, r | MAE=1.21, RMSE=2.04, r=0.98
ResNet-18 + STMap | PURE, COHFACE | MAE, RMSE | MAE=1.68, RMSE=3.11
Dual-GAN | VIPL-HR | MAE, RMSE | MAE=1.42, RMSE=2.56
rPPGNet | UBFC-rPPG | MAE, RMSE, r | MAE=0.95, RMSE=1.88, r=0.99
TS-CAN | PURE | MAE, RMSE | MAE=1.65, RMSE=3.02
Attention U-Net | UBFC-rPPG | MAE, RMSE, r | MAE=1.12, RMSE=2.01, r=0.98

## Slide 26
25
Study - 5
Result
Proposed Method | Dataset(s) | Metrics Reported | Results
3D-CNN + LSTM | VIPL-HR, PURE | MAE, RMSE, r | MAE=1.34, RMSE=2.39, r=0.97
STAttentionNet | UBFC-rPPG, PURE | MAE, RMSE, r | MAE=0.91, RMSE=1.62, r=0.99
Fusion-CNN | COHFACE, UBFC | MAE, RMSE | MAE=1.89, RMSE=3.20
HR-Transformer | PURE, VIPL-HR | MAE, RMSE, r | MAE=1.05, RMSE=1.98, r=0.99
Deep-HR | UBFC-rPPG | RMSE | RMSE=1.56

## Slide 27
26
Study - 5
Paper Name: A comprehensive review of heart rate measurement using remote photoplethysmography and deep learning
Authors: Uday Debnath & Sungho Kim (2025)
Strengths
Largest review (145 papers) covering both conventional & DL-based rPPG.
Comprehensive dataset overview.
Identifies gaps: privacy, generalization across conditions, real-time performance.
Weaknesses
Heavy focus on RGB-based approaches only (excludes IR/thermal).
Numerical results (SNR, RMSE) often summarized qualitatively — limited tabulated comparisons.
Less discussion on deployment challenges (battery, latency, integration in wearables).
Core Takeaway
This review establishes that deep learning has made rPPG heart-rate estimation far more accurate and robust than traditional methods, but motion, illumination, and skin tone diversity remain major unsolved problems. The field needs larger, more diverse datasets and privacy-conscious, real-time systems before rPPG can be widely deployed in telehealth and consumer devices.

## Slide 28
27
Phase Align Mechanism
(1.1)Put RGB and BVP on the same time grid
  Resample BVP to have exactly T samples (the length of the RGB clip) using linear interpolation.
  This keeps time linear; it does not “jump” samples (which would warp time inside the clip).
(1.2) Build a proxy pulse from RGB (phase anchor)
  Compute a simple chrominance signal: proxy = G − 0.5·(R + B)
  Intuition: this cancels most brightness/lighting changes and keeps the tiny color oscillations caused by blood volume changes (the rPPG signal).
(1.3) Clean the proxy and BVP for measuring lag only
  Apply a zero-phase band-pass filter to both the proxy and the (resampled) BVP in the cardiac band (0.7–3 Hz).
  Zero-phase means the peaks are not delayed by filtering—perfect for timing measurements.
(1.4) Measure the lag via correlation
  Slide one signal over the other (use circular shifts) and compute Pearson correlation at each shift.
  Pick the best shift s* where correlation is highest.
  If s* > 0: the proxy would need to move right by s* samples to match BVP (proxy is “late”).
  If s* < 0: the proxy would need to move left by |s*| samples (proxy is “early”).
(1.5) Apply the lag to the GT labels
  We want BVP aligned to the video proxy, so we shift the unfiltered BVP by the opposite amount: Aligned BVP = roll(BVP, −s)*
  We only used the filtered versions to measure lag. The label we train on should keep all details (full band), just moved in time.
(1.6) Save the aligned label
  Input: original RGB clip (unchanged)
  Label: Aligned BVP (same length T, now time-corrected)
before:
GT BVP: ──╭──╮─────╭──╮─────╭──╮──
PROXY: ───╭──╮─────╭──╮─────╭──╮─
^ peaks don't line up (phase lag)
after applying −s to GT:
Aligned GT: ───╭──╮─────╭──╮─────╭──╮─
PROXY: ───╭──╮─────╭──╮─────╭──╮─
^ peaks aligned (no phase lag)

## Slide 29
28
Phase Align Mechanism (Train Block 0)

## Slide 30
29
Phase Align Mechanism (Test Block 0)

## Slide 31
30
Phase Align Mechanism (Test Block 0)

## Slide 32
31
Phase Align Mechanism (PURE Dataset -> Test)

## Slide 33
32
Phase Align Mechanism (Evaluation on UBFC Dataset)
Vid -1 | Vid-10 | Vid-15
Vid-27(Previously MAX MAE) | Vid-36(Previously MAX MAE) | Vid-20
Vid-25 | Vid-30 | Vid-35
Vid-40 | Vid-42(Previously MAX MAE) | Vid-45