## Slide 1
Rafsan Jany
Korean Convergence Medical Science
Temporal Alignment Analysis of the UBFC rPPG Dataset

## Slide 2
1
Raw Code for UBFC
UBFC Dataset
(video.avi + gt.txt)
Load video + nominal FPS
Build video time axis
Define 8-second start
and
end windows
Extract ROI
Compute rPPG using CHROM
Estimate lag via cross-correlation
Compute drift = |lag_end – lag_start|
Test FPS correction

## Slide 3
2
Verify gt.txt structure and timing for one UBFC Subject
Check GT and Video timing
Video No: 01
GT loaded successfully: 1547 PPG samples, 1547 timestamps
PPG samples and timestamps are 1:1 aligned (same length)
GT PPG duration: 52.691 s
GT fps:
Video info: 1547 frames @ 29.264 fps → 52.863 s
Duration difference (video − GT): 0.172 s
Problematic Zone:
PPG: 0 → 52.691 s
Video: 0 → 52.863 s
That’s a 0.172 s offset (≈5 frames @ 29.3 fps).
So, even though there are 1547 PPG values and 1547 frames,
the last few video frames occur after the PPG stopped recording.
Visualize GT/Video timing
Loaded GT: 1547 samples
1 duplicated or non-increasing timestamps found at indices [494]
→ Adjusted duplicated timestamps by +1e-6 s increments.
Video info: 1547 frames @ 29.264 fps → 52.863 s
GT PPG duration: 52.691 s
Duration difference (video − GT): 0.172 s ≈ 5.04 frames (0.33 % of duration)
Frames within overlap: 1542 (5 trimmed)

## Slide 4
3
Measurements
Phase-Lag Estimation
To quantify alignment quality, a sign-invariant cross-correlation method is used.
sr(t) → filtered, normalized rPPG signal
sg(t) → filtered, normalized ground-truth PPG signal
Drift Measurement
The drift across the recording is defined as
Ground Truth FPS Correction Mechanism
A corrected FPS is estimated using the duration of the ground-truth PPG
The entire lag estimation process is repeated with this corrected frame timeline. For each
sequence, the drift before and after FPS correction,

## Slide 5
4
UBFC: Edge-Lag and Decision Summary
| seq id | delta fr | remain fr | decision || seq id | delta fr | remain fr | decision |
|--------|----------|-----------|--------------||--------|----------|-----------|--------------|
| vid 1 | 6.000 | 4.045 | FPS ADJUST || vid 33 | 23.000 | 0.000 | UNCERTAIN |
| vid 10 | 1.000 | 0.000 | TRIM || vid 34 | 1.000 | 0.000 | TRIM |
| vid 11 | 5.000 | 0.000 | UNCERTAIN || vid 35 | 2.000 | 0.601 | TRIM |
| vid 12 | 8.000 | 2.457 | UNCERTAIN || vid 37 | 11.000 | 0.704 | UNCERTAIN |
| vid 13 | 11.000 | 0.000 | UNCERTAIN || vid 38 | 34.000 | 0.000 | UNCERTAIN |
| vid 14 | 44.000 | 0.000 | UNCERTAIN || vid 39 | 8.000 | 0.979 | UNCERTAIN |
| vid 15 | 48.000 | 0.000 | UNCERTAIN || vid 4 | 2.000 | 0.000 | TRIM |
| vid 16 | 8.000 | 0.016 | UNCERTAIN || vid 40 | 0.000 | 0.000 | TRIM |
| vid 17 | 4.000 | 2.622 | FPS ADJUST || vid 41 | 42.000 | 0.000 | UNCERTAIN |
| vid 18 | 11.000 | 0.000 | UNCERTAIN || vid 42 | 1.000 | 0.000 | TRIM |
| vid 20 | 77.000 | 0.000 | UNCERTAIN || vid 43 | 5.000 | 0.000 | UNCERTAIN |
| vid 22 | 0.000 | 0.000 | TRIM || vid 44 | 9.000 | 1.865 | UNCERTAIN |
| vid 23 | 21.000 | 0.000 | UNCERTAIN || vid 45 | 11.000 | 0.000 | UNCERTAIN |
| vid 24 | 20.000 | 0.000 | UNCERTAIN || vid 46 | 35.000 | 0.000 | UNCERTAIN |
| vid 25 | 6.000 | 0.000 | UNCERTAIN || vid 47 | 10.000 | 0.000 | UNCERTAIN |
| vid 26 | 11.000 | 0.470 | UNCERTAIN || vid 48 | 5.000 | 0.000 | UNCERTAIN |
| vid 3 | 1.000 | 0.000 | TRIM || vid 49 | 12.000 | 0.000 | UNCERTAIN |
| vid 30 | 26.000 | 0.000 | UNCERTAIN || vid 5 | 4.000 | 0.000 | UNCERTAIN |
| vid 31 | 39.000 | 0.000 | UNCERTAIN || vid 8 | 2.000 | 0.000 | TRIM |
| vid 32 | 3.000 | 0.000 | UNCERTAIN || vid 9 | 35.000 | 0.000 | UNCERTAIN |
delta fr: timing drift expressed in number of video frames.
remain fr: number of leftover frames that do not fit into the analysis windows.
Stable (TRIM) Correctable (FPS ADJUST)
Minimal drift Drift attributed to FPS mismatch
Usable with small truncation
Problematic (UNCERTAIN)
Significant drift not explained by metadata

## Slide 6
5
UBFC: Edge-Lag and Decision Summary
Statistical Overview for UBFC
Mean drift: 15.05 frames.
• Standard deviation: 16.86 frames.
• Minimum drift: 0 frames.
• Maximum drift: 77 frames.
Remaining-frame statistics:
• Mean: 0.344 frames.
• Standard deviation: 0.867 frames.
• Maximum: 4.045 frames.
Decision distribution:
• TRIM: 9 sequences.
• FPS adjustment suggested: 2 sequences.
• UNCERTAIN: 29 sequences

## Slide 7
6
UBFC: FPS Correction Effectiveness
| seq id | Δorig | Δcorr | Improved? || seq id | Δorig | Δcorr | Improved? |
|--------|--------|--------|-----------||--------|--------|--------|-----------|
| vid 1 | 6.00 | 2.00 | True || vid 33 | 23.00 | 24.00 | False |
| vid 10 | 1.00 | 0.00 | True || vid 34 | 1.00 | 2.00 | False |
| vid 11 | 5.00 | 5.00 | False || vid 35 | 2.00 | 3.00 | False |
| vid 12 | 8.00 | 10.00 | False || vid 37 | 11.00 | 10.00 | True |
| vid 13 | 11.00 | 2.00 | True || vid 38 | 34.00 | 34.00 | False |
| vid 14 | 44.00 | 45.00 | False || vid 39 | 8.00 | 7.00 | True |
| vid 15 | 48.00 | 64.00 | False || vid 4 | 2.00 | 1.00 | True |
| vid 16 | 8.00 | 7.00 | True || vid 40 | 0.00 | 0.00 | True |
| vid 17 | 4.00 | 21.00 | False || vid 41 | 42.00 | 50.00 | False |
| vid 18 | 11.00 | 11.00 | False || vid 42 | 1.00 | 1.00 | False |
| vid 20 | 77.00 | 77.00 | False || vid 43 | 5.00 | 6.00 | False |
| vid 22 | 0.00 | 0.00 | False || vid 44 | 9.00 | 6.00 | True |
| vid 23 | 21.00 | 20.00 | True || vid 45 | 11.00 | 12.00 | False |
| vid 24 | 20.00 | 21.00 | False || vid 46 | 35.00 | 34.00 | True |
| vid 25 | 6.00 | 10.00 | False || vid 47 | 10.00 | 10.00 | True |
| vid 26 | 11.00 | 10.00 | True || vid 48 | 5.00 | 23.00 | False |
| vid 3 | 1.00 | 2.00 | False || vid 49 | 12.00 | 12.00 | False |
| vid 30 | 26.00 | 27.00 | False || vid 5 | 4.00 | 1.00 | True |
| vid 31 | 39.00 | 39.00 | False || vid 8 | 2.00 | 2.00 | False |
| vid 32 | 3.00 | 3.00 | False || vid 9 | 35.00 | 35.00 | False |
∆orig: drift before FPS correction.
∆corr: drift after FPS correction
Summary for UBFC:
• Total sequences analyzed: 40.
• FPS correction improved drift in 14 sequences.
• FPS correction did not help in 26 sequences.

## Slide 8
7
UBFC: Vid_14
| seq id | Δorig | Δcorr | delta fr | remain fr |
| seq id | 44.00 | 45.00 | 44.000 | 0.000 |

## Slide 9
8
UBFC: Vid_14

## Slide 10
9
UBFC: Vid_14

## Slide 11
10
UBFC: Vid_15
| seq id | Δorig | Δcorr | delta fr | remain fr |
| seq id | 48.00 | 64.00 | 48.000 | 0.000 |

## Slide 12
11
UBFC: Vid_15

## Slide 13
12
UBFC: Vid_15

## Slide 14
13
UBFC: Vid_20
| seq id | Δorig | Δcorr | delta fr | remain fr |
| seq id | 77.00 | 77.00 | 77.000 | 0.000 |

## Slide 15
14
UBFC: Vid_20

## Slide 16
15
UBFC: Vid_20

## Slide 17
16
UBFC: Vid_31
| seq id | Δorig | Δcorr | delta fr | remain fr |
| seq id | 39.00 | 39.00 | 39.000 | 0.000 |

## Slide 18
17
UBFC: Vid_31

## Slide 19
18
UBFC: Vid_31

## Slide 20
19
UBFC: Vid_41
| seq id | Δorig | Δcorr | delta fr | remain fr |
| seq id | 42.00 | 50.00 | 42.000 | 0.000 |

## Slide 21
20
UBFC: Vid_41

## Slide 22
21
UBFC: Vid_41

## Slide 23
22
Appendix
Abbreviation | Full Form | Meaning / Description | Context in Discussion
BCG | Ballistocardiography | Measurement of tiny body movements caused by cardiac ejection of blood (mechanical action of the heart). | Used as the start reference signal in Yoshioka et al. (2020) via 24 GHz radar to compute PTT.
PPG | Photoplethysmography | Optical measurement of blood volume changes in tissue using a light source and detector (usually contact-based). | Conventional contact sensor reference for pulse arrival.
iPPG | Imaging Photoplethysmography | PPG signal extracted from video frames (facial brightness changes), without physical contact. | Used in Yoshioka et al. (2020) for noncontact pulse detection.
rPPG | Remote Photoplethysmography | General term for noncontact PPG obtained from camera images (essentially same as iPPG). | The main signal type in current research focus.
PTT | Pulse Transit Time | Time taken for the arterial pulse wave to travel between two sites (from heart to face). | Key physiological metric; shorter PTT means higher arterial stiffness or BP.
PAT | Pulse Arrival Time | Time between ECG R-wave (electrical heart activation) and PPG pulse arrival; includes pre-ejection period (PEP). | Used in both papers as a surrogate of true PTT.
PEP | Pre-Ejection Period | Time between the ECG R-wave and the actual mechanical ejection of blood from the heart. | Present in PAT, but not in PTT (BCG avoids this).
ECG | Electrocardiography | Electrical recording of heart activity, especially used to detect the R-wave for timing. | Contact reference for PAT in Block et al. (2020).
BP | Blood Pressure | Force exerted by circulating blood on arterial walls. | Physiological parameter correlated inversely with PTT.
SBP | Systolic Blood Pressure | Maximum arterial pressure during heart contraction. | Strongly correlated with PTT (R ≈ −0.6).
DBP | Diastolic Blood Pressure | Minimum arterial pressure during heart relaxation. | Weak correlation with PTT (R ≈ −0.2).
ROI | Region of Interest | Specific area in an image or video used for signal extraction (e.g., cheek or forehead). | In iPPG, face ROI used for green-channel brightness analysis.
FIR | Finite Impulse Response | Type of digital filter used for signal smoothing and noise reduction. | Applied to iPPG signals before peak detection in Yoshioka et al. (2020).
cPTT | Conventional Pulse Transit Time | PTT derived from ECG–PPG or PPG–PPG pairs using contact sensors. | Defined in Block et al. (2020) as traditional, contact-based methods.
dPTT | Differential Pulse Transit Time | Time difference between two distal PPGs (e.g., ear–toe). | Represents the difference of two PTTs, not a true PTT.
PATfoot / PPG foot | — | The waveform onset (foot) used as a reliable timing marker for pulse arrival. | Identified in Block et al. (2020) as more consistent than the peak.